## Slide 1: Agilex I-Series F-Tile Demo designs Supporting Documentation V1.2 Targeted for ACDS 21.3
Peter Schepers
Technology Specialist FAE High Speed Interfaces
November 30th, 2021

## Slide 2: Introduction & Motivation
This document serves as supporting documentation for the various F-tile demo designs.
All F-tile demo designs (except Superlite II variants) follow a similar configuration and can have different number of channels, different clocking, using fec or not, FGT or FHT etc. but the look and feel is always the same, both from RTL implementation as well from software implementation.
The RTL is “PHY” based which means a number of PHY’s each with various amounts of channels can be instantiated. A full description of the designs is maintained in the file Description of designs.xls which is maintained on the Intel Forum Agilex I-Series Demo page https://community.intel.com/t5/FPGA-Wiki/High-Speed-Transceiver-Demo-Designs-Agilex-I-Series-F-Tile/ta-p/1315123
The software is written in such a way that there is a single main.c file and supporting files that is being re-used by all designs (whether FEC is used or not) and the parameterization is done using the parameters.h file. Those software files are also maintained on the Intel Forum Agilex I-Series Demo page https://community.intel.com/t5/FPGA-Wiki/High-Speed-Transceiver-Demo-Designs-Agilex-I-Series-F-Tile/ta-p/1315123
This allows to maintain a single set of source files to be used across all designs and only very little parameterization is required. E.g. to move from a design that is using 2 PHY’s with 4 channels each with PAM4 without FEC to a design that is using 3 PHY’s with FEC only very few lines have to be modified in the parameters.h file. Examples of those are also maintained in the software section on the Agilex I-Series Demo page.

## Slide 3: Introduction & Motivation (continued)
Throughout the remainder of this document one of the example designs is being used.
The example being used in this case is the Agilex I-Series PCIe Devkit demo design with 2 PHY’s each having 4 independent channels at 53 Gbps PAM4 with KPFEC (544,514) enabled.
Each PHY is connected to the QSFP-DD connectors on the board.

## Slide 4: F-Tile Soft PRBS RSFEC demo design Goals.
  Use Agilex I-Series PCIe Development kit as platform for demonstration.
    Uses 2 Native PHY’s with each 4 independent physical lanes connected to QSFPDD0 and QSFPDD1 and each channel configured in RSFEC 53Gpbs PAM4 using 8 FGT’s located in Quad 3 and Quad 1
    As there is only one clock source on the board both phy’s are clocked from the same referenceclock.
  Uses dedicated txrx_pcs_64b66b_fgt module which instantiates all relevant additional logic required for RSFEC operation.
  User data width is 128-bits per physical lane.
  Since RSFEC is used in the PHY Direct IP, system PLL clocking is used. And both Tx and Rx user interface are clocked by the System PLL/2 clock which is running at 53.125Gbps/128 = 415.0390625 Mhz.
  Each channel is fully independent and can be indepently resetted without impacting the other channels.
  Uses Release Reset IP (recommended for all S10 designs from 19.1 onwards)
  Design uses a Qsys system with Nios II Processor to control the PHY Direct IP’s used in the PHY and control all other logic (like temperature measurement etc.)
  To create the 2x4 128 bit user data 128-bit soft PRBS generators and 128-bit PRBS checkers are being used. Supported PRBS patterns : PRBS-7, PRBS-13, PRBS-23, PRBS-31.
  Each 128-bit Prbs Generator will use a different seed to avoid the same pattern being sent on the 512 bit bus going to each PHY.

## Slide 5: Goals (continued)
  Uses Scrambler/Descrambler on top of the PRBS pattern as a scrambler is required on user data in combination with the FEC. Even though mandatory for FEC the scrambler can be dynamically enabled/disabled. Each virtual lane (64 bit) has it’s own scrambler/descrambler. Scramblers/Descramblers used are self synchronizing as used by Ethernet IEEE interfaces with polynomial 1 + x^39 + x^58
  Supports serial loopback (note that if Serial loopback has been set it will remain set even after a reset or after restarting the software).
  Supports reverse parallel loopback
  Additional control signals required for the RSFEC operation are also generated in the design in module txrx_pcs_64b66b_fgt
    tx_pcs_ready : low every 17th clock cycle (32/34 ratio) (note that different tx_pcs_ready cadence is required for (528,514)
    am_pulse : 2 clock periods every 40960 parallel clock cycles (note that am pulse width and am pulse period is different for different configurations).
  Used 2 different AVMM interfaces to the PHY direct IP : the transceiver reconfiguration interface and the transceiver datapath interface.
  Reports errorcount and calculates BER based on the received data.
  Extensive FEC statistics are provided for each virtual lane and physical lane (see screenshots further for information shown).
  This version enables Internal noise that can by dynamically reconfigured (8 noise modules are instantiated).
  Displays measured core temperatures.

## Slide 6: Goals (continued)
  Uses PrbsAlarm signal and PrbsAlarmCount : the PrbsAlarm signal will be asserted when the PrbsLock will go down (due to external causes e.g. cable pull/plug in) and remain asserted until a reset errorcount or reset of the phy is being done. This allows to capture any events that could occur that could bring down a link for a period of time to keep track of this.
  Uses PrbsAlarmCount : Counts the amount of times the PRBSAlarm has occurred.
  Uses Rx AM Lock Alarm signal and : the Rx AM Lock Alarm signal will be asserted when the FEC looses lock (due to external causes e.g. cable pull/plug in) and remain asserted until a reset errorcount or reset of the phy is being done. This allows to capture any events that could occur that could bring down a link for a period of time to keep track of this.
  Uses Rx AM Lock Alarm Count : Counts the amount of times the FEC has lost lock.
  Through NDME Toolkit support is automatically available (from 21.3 onwards and using patch 0.16)
  Reads out and print out PMA settings for all channels
  Allows to find the optimum Transmit PMA settings (VOD, Pre-emphasis) using PMA sweep function.
  Option ‘c’ allows to provide updates on the selected channels in terms of BER and FEC statistics, this can be used over time to trace any events going on and can be further post-processed.
  Option ‘#’ builds a “FEC error tree” live on the screen.
  Allows to mute the FGT transmit (to mimic e.g. a cable pull)
  Contains several stress test functions
  I2C support for the QSFPDD modules for the 4 F-tile Demo board. (not supported yet for the PCIe Devkit as the I2C control is handled by dedicated I2C controller)
  Includes Testbench for a single PHY configuration.

## Slide 7: Future Enhancements
  Add I2C support for the QSFPDD modules for PCIe devkit. Add F-tile temperature readout (requires production silicon)
  Control Invert Tx and Rx Polarity on all lanes and per phy (functionality implemented but need further debug)

## Slide 10: F-Tile Phy Direct IP (Common Datapath)

## Slide 11: F-Tile Phy Direct IP (Tx Datapath Options)

## Slide 12: F-Tile Phy Direct IP (Tx Datapath Options cont.)

## Slide 13: F-Tile Phy Direct IP (Rx Datapath Options)

## Slide 14: F-Tile Phy Direct IP (Rx Datapath Options cont.)

## Slide 15: F-Tile Phy Direct IP (RS-FEC)

## Slide 16: F-Tile Phy Direct IP (Avalon Memory-Mapped Interface)

## Slide 17: Reset Control
  Each Phy Direct IP has a tx_reset and an rx_reset (so 8 tx_reset’s and 8 rx_resets in total)
  The Reset control is entirely handled by the Nios and is using also the corresponding tx_reset_ack and rx_reset_ack status signals.
  Since each channel is independent, each channel can be independently resetted without impacting the other channels.

## Slide 18: Channel Register Set
  The design is using 2 custom .qsys component that can be parameterized. The components are called “Channel Register Set” (using channel_reg_set_hw.tcl) and “Phy Register Set” (using phy_reg_set_hw.tcl) are available in the default group section of the Qsys library.
  These components can be parameterized to the number of phys and channels there are instantiated in the design and makes the generation of the Qsys system much more streamlined.
  As in this design 2 phy’s are being used the number of phy’s is set to 2 in the “Phy Register Set” and since it uses single lanes the amount of AVMM per phy is set to 4.
  Since each phy has 4 lanes the number of register set has been set to 8 in the “Channel Register Set”.

## Slide 19: Timing Closure (Setup)
The design is fully constraint without any timing violations
Compiled for AGIB027R29A1E2VR0

## Slide 20: Timing Closure (Hold)
The design is fully constraint without any timing violations
Compiled for AGIB027R29A1E2VR0

## Slide 21: Native Phy Debug Master Endpoint Interface
In addition to the AVMM interface the Native PHY also enable the Native Phy Debug Master Endpoint interface which can also be accessed through the Qsys system due to the addition of the jtag_debug_module.
Access to the Native Phy Debug Master Endpoint interface can be done through System Console totally in parallel while the Nios controller(s) are being used.
The Native Phy Debug Master Endpoint interface can be used for advanced debugging and reporting (see further) .
The major advantage of having the Native Phy Debug Master Endpoint interface is that it allows to run directly the Universal Toolkit (see further).

## Slide 22: Nios II Control & Monitoring
The Nios II controller is used to control and monitor the design using the Nios II terminal.
  Display status signals for each of the channels
    Tile/Quad information
    Encoding (PAM4/NRZ and gray and/or 1/1+D encoding)
    RSFEC Statistics
    RX AM Lock Alarm Count
    PrbsLock Alarm and PrbsLockAlarmCount
    Freq_Locked
    Pll_locked
    Tx_ready/Rx_ready
    Serial Loop + Reverse Parallel Loop
    Channel Type
    Connection Type
    Rx Polarity Inversion
    Tx Polarity Inversion
    Number of biterrors.
  Select which PRBS pattern should be used (PRBS-7, PRBS-13,PRBS-23 or PRBS-31) on each channel
  Displays the bitrate based on measured reference clock frequency and reference clock multiplication factor.
  Displays also the recovered clock frequency (of lane 0 only). Note that if lane 0 has no connection or is is not in serial loopback the measured recovered clock frequency is a random number as the CDR is not locked to anything.

## Slide 23: Nios II Control & Monitoring (continued)
  Control Serial Loopback on all lanes and per phy
  Control Reverse Parallel Loopback on all lanes and per phy
  Error insertion : Soft PRBS Biterror (Pre-FEC) or error insertion through RS-FEC directly.
  Displays the number of biterrors and the BER.
  NEW Reads out and print out PMA settings for all channels
  New Control Invert Tx and Rx Polarity on all lanes and per phy
  New PMA tuning : Allows to find the optimum Transmit PMA settings (VOD, Pre-emphasis) using PMA sweep function.
  Stress Tests : 4 different stress tests are avalailable (see dedicated slide)
  Displays the time the test has been running on the Transceiver Block.

## Slide 24: Nios II Control & Monitoring (to be added)
  Measures the temperatures of the core (supported) and the transceiver tile (to be added)
  Dumps I2C information of connected modules and cables like Vendor, part number, cable length, temperature of the module. (to be added for PCIe devkit)
  Allows to dump the I2C page Lower page and Page 00h registers of the selected module/cable (to be added for PCIe devkit)

## Slide 25: Stress Tests
Option ‘L’ provides a submenu to perform the following “stress tests”:
Test 1 : Reset selected PHY 1000 times and verify it comes up ok
Test 2 : Reset selected PHY 1000 times and verifies both PHY’s come up ok.
Test 3 : Do rx_reset only of the Selected PHY and verify it comes up ok.
Test 4 : Perform AVMM accesses to various registers using both xcvr_reconfiguration_interface as pdp_interface (1000 times)
Test 5 : Mimic cable pull/plug-in using Tx mute option on local phy and verify if remote PHY comes up properly

## Slide 26: Nios 2 Output in Nios II SDK Shell

## Slide 27: PHY 0 connected to PHY1 with 2.5 Meter QSFP-DD cable at 53.125 Gbps

## Slide 28: PHY 1 connected to PHY0 with 2.5 Meter QSFP-DD cable at 53.125 Gbps

## Slide 29: Readout of temperature and Internal Noise (if available)

## Slide 30: Available commands

## Slide 31: Show PMA settings (option ‘e’) using 2.5 meter DAC cable

## Slide 32: Sweep PMA function (option ‘u’)

## Slide 33: Continuous Update of BER and FEC statistics (option ‘c’)

## Slide 34: FEC Error Tree (option ‘#’)
This will be build “live”, note that if a number is in red it means at least 1 overrun has occurred for that particular bin (each bin is only 256 words, so for the lower bins the software can’t read fast enough and print at the same time to prevent an overrun. If only 1 overrun has occurred the value is correct though (so the higher bins values are correct)

## Slide 35: Readout of the I2C information (to be added on PCIe devkit)
Every time a status update is done all QSFP-DD modules will be checked if anything is plugged in and if this is the case the I2C information will be readout.
See screenshot below showing various module and cables connected in the the system.
Information provided is Vendor, Part Number, temperature for modules and cable length for QSFP-DD cables or QSFP cables.
One can dump the entire I2C Lower Page and Page 00h using option ‘{‘

## Slide 36: Board setup
Make connections to the QSFPDD0 and QSFPDD1 (Using loopback modules, optical modules or cable).
Connect micro-USB Cable to J8 in order to use onboard USB-Blaster II.
Power on the board
All designs so far use the default clock frequency of 156.25 Mhz. Not required to use clock control GUI to change clocks.
Download ‘Devkit_Demo.sof’ to the AGIB027R29A1E2VR0 device using QII 21.3 programmer

## Slide 37: Running the software on Windows10
This is when you want to run the software provided as .elf file (part of the deliverable) Do the following :
  Start a Nios II command Shell (can be found in the Quartus installation (e.g. C:\quartus_21_3\nios2eds) and go to the directory where the .elf and run1.bsh files are located.
  Since 21.3 Nios II terminal is using WSL, a quick way to go to the selected directory is to copy the complete path using windows explorer and in the Nios 21.3 terminal you type cd "$(wslpath “ => then you paste the path you copied (using right mouse click) => and end with typing ")“
    e.g. cd "$(wslpath " C:\ALTERA\Reference_Designs\PRBSTEST\Agilex\I_PCIe_Devkit\Agilex_prbs_2x4ch_kpfec_FTILE_53Gbps_fract\software\app\Agilex_xCh")“
  Since the quartus archive is restored in windows the files need to be converted from Dos to Linux. To do so either use “dos2unix –k *” or run the provided .bsh file “./convert.bsh” (note option –k keeps the original date of the file intact).
  Type In The Following Command : “./run1.bsh” This will set the JtagSpeed to 16M ,download the .elf file and start the downloaded Nios II code inside the main program memory.

## Slide 38: Rebuilding the software on Windows 10
In order to rebuild the software do the following (using QII 21.3 or later):
Start a Nios II 21.3 Command Shell
  go to the ../software/app/Agilex_xCh directory (which is part of the archive) using the method descriped on the previous slide
  Run the bash file ./convert.bsh (this will also convert the files in the bsp folder)
  Run ./create-this-app .This will compile the system libraries (in the bsp folder), compile the software code (main.c and a number of other .c files in this case) and produce a Nios II executable.
If you make any changes to the software you need to rebuild by typing “make” in the Nios II 21.3 shell (after having created the software a first time)
To run the software : type In The Following Command : “./run1.bsh” This will set the JtagSpeed to 16M and download the Nios II code to the FPGA and open up the terminal.

## Slide 39: Running the software on Linux
This is when you want to run the software provided as .elf file (part of the deliverable) Do the following :
  Start a konsole with enough memory (e.g. “arc submit -i node/"memory>=128000" -- konsole”)
  Make sure all restored files are unix files and are executable (use “./convert.bsh”)
  Open an acds shell (e.g. “arc shell acds/21.3”)
  Start a Nios Command Shell (e.g. “/p/psg/swip/releases/acds/21.3/170/linux64/nios2eds/nios2_command_shell.*”) One can figure out the path using “which quartus” while being in the acds shell
  Download the .elf file using command “nios2-download -r -c 1 -d 1 -i "0" -g Agilex_xCh.elf” Note that this assumes the device is connected to USB-Cable with index 1. If another index is used, change accordingly.
  Next use “nios2-terminal -c 1 -d 1 -i "0" |tee output.log” to run the software from program memory.

## Slide 40: Rebuilding the software on Linux
In order to rebuild the software do the following (using QII 21.3 or later):
Start a Nios II 21.3 Command Shell using the steps on the previous slide
  go to the ../software/app/Agilex_xCh directory (which is part of the archive)
  Run the bash file ./convert.bsh (should already have been done)
  Run ./create-this-app .This will compile the system libraries (in the bsp folder), compile the software code (main.c and a number of other .c files in this case) and produce a Nios II executable.
If you make any changes to the software you need to rebuild by typing “make” in the Nios II 21.3 shell (after having created the software a first time)
  To run the software :
  Download the .elf file using command “nios2-download -r -c 1 -d 1 -i "0" -g Agilex_xCh.elf”. Note that this assumes the device is connected to USB-Cable with index 1. If another index is used, change accordingly.
  Next use “nios2-terminal -c 1 -d 1 -i "0" |tee output.log” to run the software from program memory.

## Slide 41: Using Transceiver Toolkit (need patch 0.16 on top of 21.3)
To start the Transceiver Toolkit simply start it from the Tools Menu in Quartus (with the project loaded). This will automatically detect the design and start up the Transceiver Toolkit which allows you to run further tests in optimizing the PMA settings, do autosweeps etc.
Make sure to stop all traffic running in TTK and close the TTK before going back to the Nios terminal to continue with the design (If the hard PRBS generator and checker have been enabled during testing those channels will show errors (which is normal). Using option ‘q’ these errors can be cleared

## Slide 42: Signaltap II Debug Example
The design contains a number of signaltap instances
Signaltap II acquisition can be done simultaneously with Nios II control.

## Slide 43: How to run a simulation using Questasim/Modelsim (1/4)
Open the project using Quartus in directory <restored_project>/simulation/mentor (DO NOT USE THE ORIGINAL PROJECT AFTER RESTORING THE ARCHIVE FOR THE SIMULATION)
Make sure the IP settings are set correctly (see slide (3/4). IP settings are not fully governed by .qsf only, hence the additional check to be done to make sure they are correctly set
Run an Analysis and Elaboration (this generates the __tiles files which are mandatory for the simulation) and also regenerates all .ip files and .spd files required for the simulation.
From the Quartus Menu Start Tools => Generate Simulator Setup Script for IP…

## Slide 44: How to run a simulation using Questasim/Modelsim (2/4)
In the window that pops-up, remove the mentor in the path name so that you get <restored_project>/simulation/
Make sure “use top-level entity names from Quartus project” is not selected (in 21.3 this is already remove as an option)

## Slide 45: How to run a simulation using Questasim/Modelsim (3/4)

## Slide 46: How to run a simulation using Questasim/Modelsim (4/4)
Go to the simulation/mentor folder and launch questasim e.g. using the following command arc submit -i questasim/2020.4 questasim_sver-lic priority=100 -- "vsim -i -64“
Type “sim.do” => this will do the entire simulation.
In case modifications are made to the source files you can rerun the simulation using “resim.do”

## Slide 47: Deliverables
Quartus 21.3 B170 archive which contains the demo design files, the software source files, files required to run the simulation
The testbenches and project files required for simulation can be found after restoring the archive: <restored_project>/simulation/mentor
The software source files can be found after restoring the archive in the <restored_project>/software/app and <restored_project>/software/bsp folders/
SOF File
Devkit_demo.elf File (Software)
Readme.txt file

## Slide 48: Status & Revision
V21.3 : November 30th, 2021
  Added internal noise logic to the design
  Added RX AM lock statistics.
  Major upgrade to the software functions
V21.3 : October 8th, 2021
  Upgraded to 21.3
V21.2 : September 16th 2021.
  Initial release tested with QSFP-DD 2.5 meter cable
  Note that after starting the design or after a reset of PHY it can happen that the lane does not come up (rx_ready not asserted). If this occurs, one can reset the channel in question using command ‘~’. This issue is fixed in 21.3
  Serial loopback is also not working with 21.2 (fixed in 21.3)

## Slide 49: Feedback and/or Questions?
Peter Schepers (peter.schepers@intel.com )
+32 495 57 32 22