## Slide 1: Arria10 GX ‘SuperLite II V4’ Demo Design V20.4 for the Arria10 GX SI Board 4 Lanes @ 10.3125 Gbps routed to the QSFP+ Module
Peter Schepers
Technology Specialist FAE High Speed Interfaces
March 4th, 2021

## Slide 2: Introduction & Motivation
This design illustrates how to use the Superlite II V4 concept on Arria10 GX
The V4 version of Superlite II is based on the V2+V3 version.
The V2 version uses a valid signal in combination with the transmit data and there is also a ready signal provided which can potentially halt the transmit traffic for a short interval (based on filling level of Transmit FIFO). This interface is equivalent to the Avalon Streaming Interface.
The V3 version adds additional functionality :
  Link information is exchanged between the local and remote side and results in a LinkUp when both local and remote side are aligned.
  XOFF is used in order to allow for backpressure or Flow Control: ask remote side to stop sending traffic (when local side e.g. is not capable of receiving the data).
  Because of the exchanges between local and remote side the protocol is now a fully bidirectional protocol (V1 and V2 versions could be used fully unidirectional)

## Slide 3: Introduction & Motivation
  The V4 version is the version where transmit datapath is clocked with a single clock derived from the transceiver. This simplifies the Tx statemachine and FIFO implementation and has a significant reduction of the latency.
  Additional features added in this latest V4 version :
Insertion and detection of Lane Identification: each lane has it’s own unique identifier. So if lane swap or lane re-ordering occurs the information received in terms of lane identification allows to automatically recreate the original data pattern. This helps in not having to worry about how the lanes are routed in layout or how cables are connected.
Added GENERIC parameter SIMPLEX which when set to true does not perform handshaking with the remote side and allows SIMPLEX operation (even when using Duplex transceiver). When parameter SIMPLEX is set to true, Linkup will be declared when LaneAligned is achieved locally.
Simplified exchange of control characters for flow control.
Tested interoperability with equivalent Superlite II V4 versions on S10TX (E-tile) and S10 GX (H-tile).
Latency measurement is inherently part of the protocol now.

## Slide 4: How to use Superlite II V3 in Packet mode ?
  By nature the Superlite II V3 is using streaming data (Avalon streaming based) so not framed or packetized . One could however support also a framed mode (or packet mode) by using one of the lanes to transport the packet related information (SOP, EOP, etc) . This does require an additional lane to provide the packet overhead information. This concept has been succesfully implemented on Stratix V GX (with 11 lanes) and can easily be repeated on Arria10 (with higher rates and including KR-FEC).

## Slide 5: ‘SuperLite II V4’ Concept

## Slide 6: ‘SuperLite II V4’ Concept
Transport data from point A to point B as simple as possible multiple bidirectional serial links. Note that the number of lanes in each direction do not have to be equal.
V3 version of the protocol exchanges information between local and return side (handshaking) as well as XON/XOFF control (backpressure)
On the transmit side data will only be written in the FIFO when the valid signal is asserted, the fifo also can issue a backpressure signal (indicated by the ‘ready’ signal to indicate if data can be transmitted. This is equivalent to the Avalon Streaming interface.
When XOFF is received from the remote side, all traffic will be halted on the local side (link remains up though).
The transmit datapath is entirely clocked on the clock derived from the transceiver (transmitted line rate/66).
On the receive side it will be based on the recovered clock (received line rate/66) with data valid. The combination of data valid with the recovered clock is frequency locked to the clock used at the transmit side.
Uses 64/66 Encoding in combination with scrambling.
Multiple lanes are bonded, there is no real limit on the number of lanes that can be used, apart from potential limitations to compile very large number of lanes. Typically 4 or 10 lanes will be used. Also a single lane is possible.
For word alignment and lane alignment idle characters and alignment characters will be sent at regular intervals

## Slide 7: ‘Superlite II V4’ Concept (continued)
The Superlite II V4 TX module will automatically pause Tx user data if needed to insert idle and alignment characters and will also pause Tx user data based on the “ready” received from the Native PHY (as it is working in overspeed). So the userdata needs to be able to immediately stop sending traffic. If this is not possible one can add an additional FIFO with a slower running write clock.
User data is always 64 bit per lane because of the 64b66b encoding.
Efficiency is calculated as (Read_Length)/(Read_Length + Idle_Length) * 64/66, so e.g. for the parameters used in the demo design : 1056/(1056+7) * 64/66 = 96.33%. By increasing the Read_Length the efficiency/net rate can be increased.

## Slide 8: ‘SuperLite II V4 4 lane Demo Design
Goals :
  Demonstrate the Superlite II V4 concept on Arria10 GX
    Use Arria10 GX Signal Integrity board as platform for demonstration.
      Uses the 4 channels routed to the QSFP+.
      Using 2 separate boards is also possible if connection through QSFP+ module is done (this method was used to test against S10 TX e.g.)
    Line rate in this demo is 10.3125 Gbps per lane (because of the QSFP+ module) but could be go all the way up to maximum datarate allowed.
    4 lanes will be used, therefore aggregate line rate is 40 Gbps.
    User data width is 256-bits (64 bits per lane)
    Actual throughput depends on the configured “read time” and “idle time” parameters. In the demo the “read time” is 1056 clock cycles and “idle time” is 7 clock cycles but these can be easily changed. The “read time” would normally be set to a higher value like e.g. 67584 clock cycles in order to increase the efficiency.
    Actual throughput is measured in the design by measuring the data_valid received in combination with the clock.
    To create the 256 bit user data a combination of different counterpatterns and prbspatterns are used across the 4 lanes.

## Slide 9: Goals (continued)
Goals :
  The user data is generated based on the line_rate/66 Mhz clock generated by the Native PHY (156.25 Mhz) . As it receives backpressures from the Superlite IV Tx module the data will be halted at specific times (every “read-time”).
  Use Reconfiguration Management Interface for Native PHY and LC PLL through QSYS system.
  Through NDME Transceiver Toolkit support is automatically available.
  Use Nios II processor as controller/monitor
  Allows to perform ODI Measurement from within the Nios command shell, measuring both 2D eye as well as bathtub curve on the selected lane and provide statistics (Eye height, width etc).
  The PMA settings of the lanes can dynamically be modified
  Includes Testbench

## Slide 10: ‘SuperLiteII V4’ Resources for 4 Lanes
SuperliteII V4 TxRx Module Resources
Note : A large % of the resources is taken by the additional logic enabled in the Native PHY for debug purposes (like NDME etc) This is additional debug logic that is not required for a full design). The NPHY resource numbers are highlighted to show that this is around 50%.
  ~ 2100 ALUTs
  ~ 1400 ALM’s
  ~ 2100 Dedicated logic registers
  0 M20K’s
  130 ALM’s used for memory

## Slide 11: Blockdiagram

## Slide 12: ‘txrx_pcs_64b66b’ Detailed blockdiagram

## Slide 13: Tx Path
A datastream is generated at a clock of 156.25 Mhz @ 256 bit when DataIn_ready is high. The datapattern is a combination of 4 60-bit Prbs-23 (each with their own starting value) and one 16-bit counterpattern.
  The 16-bit counterpattern is spread across the 4 lanes, 4 bits per lane. This is to make sure any deskew on the lanes would be immediately spotted.
Since idle and alignment characters have to be inserted at regular intervals the data stream will be halted at regular intervals in order to insert the required idle and alignment characters. This is indicated by the Superlite II TX module by the DataIn_ready signal.
In case XOFF is received from the Remote side the DataIn_Ready signal will be low to avoid any traffic being sent.
Single biterrors can be inserted using inserterror input. As there is one PRBSGenerator per lane, the biterror insert will produce 4 bit-errors at a time in fact.
This data is presented to the Superlite II Tx Module
The data is written into the TxFifo using the 156.25 Mhz as write clock and using the DataIn_Valid as write-enable.
The read clock for the TxFifo is the same 156.25 Mhz clock which is driven from the tx_clkout of the transceiver PHY
During the intervals that readenable is deactivated, idle characters and the alignment characters will be inserted in the datastream which is fed to the 64b66b encoder blocks.
If no valid data is present idle characters will be sent.

## Slide 14: Tx Path (continued)
The 64b66 encoding is very straightforward : bits 65..64 are set to “10” for control data and “01” for data (so neutral disparity)
In terms of idle character a value of “1C1C….1CBC” is being used. The alignment character is sent as the last control character. The lower 16 bits of this control word (at the alignment position) encodes the status of the link in addition to the alignment indication.
If no local alignment has been found : the last control word sent is “..7C7C”
If local wordalignment has been found : the last control word sent is “..FD7C”
If XOFF is being sent to the remote side : the last control word sent is “..5C7C”
Lane Alignment coding (B<i> is the byte)
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
Lane Identity | Latency Count Tx | 7C | 7C | 7C | 7C | FD/5C/7C | 7C

## Slide 15: Tx Path (continued)
The resulting 66-bit is sent to the Native PHY where the scrambler is enabled and the gearbox converts it from 66-bit to 64-bits PMA
In order to make sure there is DC balance and enough transitions present on the serial links a selfsynchronizing scrambler is used, in this implementation the scrambler of the Enhanced PCS is used. The scrambler will scramble only the 64 databits (the framing bits on bits [65..64] are not scrambled since they are required for the framing. The polynomial used for the scrambler is 1 + x^39 + x^58 according to the IEEE.
Finally the data is serialized in the Native PHY (using 64-bit serializer) and sent out as serial datastreams (10.3125 Gbps per lane).

## Slide 16: Rx Path
After deserialization the data is presented to the Rx Block Synchronizer inside the Native PHY where it will automatically align on the incoming valid 66 bit words.
This is all happening on all lanes at the same time and everything is clocked based on the recovered clock of channel 0. The phasecompensation FIFOs inside the 10G PCS will be used to make sure lanes 1 to 4 have the right phaserelationship. Note that the recovered clock on lanes 1 to 4 are the same frequency as lane 0 but have a different phase relationship, hence the need for the phasecompensation FIFOs.

## Slide 17: Rx Path (continued)
Based on the position of the alignment word, the delay for each lane is measured, the statemachine inside the Rx_path_deskew module will use the information of that measured delay to control a special Rx FIFO signal “rx_fifo_rd_en” on all RxFIFO’s inside the Native PHY to deskew all the lanes.
Once lane alignment is achieved the 256-bit combined data in addition with a data valid signal will be sent to the data verifier.
Here PRBS and counterverification will take place and single biterrors will be counted.
Prbslocked is asserted when 128 consecutive valid Prbs-23 60-bit words have been received on each of the lanes and de-asserted when 128 consecutive non-valid Prbs-23 60-bit words have been received.
Countlocked is asserted when 128 consecutive valid 16-bit counter words have been received on the parts of the lanes they were received.
There are 4 60 bit PRBS Verifiers (one for every lane) and 1 16-bit CountVerifiers to validate the 256 bit data.

## Slide 18: Rx Path (continued)
The V3 version adds an additional Rx State machine to the logic to determine the local Rx state and it depends on the incoming “alignment” control word
If last control word received is “…FD7C” it means the remote side has reached Wordalignment, if local side also has reached wordalignment this results in Linkup to be asserted, indicating that both sides are up and running. This can be used as the trigger to sent data across e.g.
If last control word received is “…5C7C” it means an XOFF has been received from the remote side, this will be forwarded to the local transmitter to stop generating traffic on the local side.
(See Flow chart on next slide for more details)

## Slide 19: Control Characters used in combination with XOFF

## Slide 20: Transceiver Configuration (1/4)
A 4 lanes Duplex Native PHY is selected. Using 10G PCS (Enhanced PCS), 66 bit FPGA interface width, 40 bit PCS/PMA width and a datarate of 10312.5 Mbps from a 644.53125 Mhz referenceclock.

## Slide 21: Transceiver Configuration (2/4)
In order to use the Rx FIFO for deskewing the lanes the optional signal “rx_enh_fifo_rd_en” must be enabled (the other fifo status signals are optional).
RX FIFO mode should be set to “Basic”

## Slide 22: Transceiver Configuration (3/4)
Tx Scrambler (with Seed pattern shown below) and Rx Descrambler should be enabled.
Block Sync should be enabled.

## Slide 23: Transceiver Configuration (4/4)
To enable a full set of debug capabilities (including Toolkit functionality) all the options as shown below are enabled. Note that in a final design these are not all mandatory and can be disabled to save resources.

## Slide 24: ATX PLL Configuration

## Slide 25: Transceiver TX Reset Controller
Uses the recommended timings
Note that the Reset controllers work in combination with the TRS (Transceiver Reset Sequencer) which is automatically inserted by Quartus in the design (transparent to the user).

## Slide 26: Transceiver Rx Reset Controller
Starts from Arria10 default settings
Increase default value of rx_digitalreset to 40000 ns or higher

## Slide 27: Reconfig Management Interface.
The Native PHY as well as the ATX PLL have an Avalon MM Interface which allow full control of the register space of the transceiver and the ATX PLL.
The AVMM used for the Native PHY is using shared addressing for all channels and provides one interface to the .QSYS system.
The AVMM used for the ATX PLL provides another separate interface to the .QSYS system.
This design is using a QSYS system which transparently maps the AMM interfaces to the Native PHY and the ATX PLL.
The component created for this in QSYS is called “reconfig_mgmt” and the reconfig_mgmt_hw.tcl file included in the project describes it’s implementation.
You can verify it’s content by editing the reconfig_mgmt component.

## Slide 28: NDME Interface
In addition to the AVMM interface the Native PHY also enables the NDME interface (Altera Debug Master Endpoint) which can also be accessed through the Qsys system due to the addition of the jtag_debug_module.
Access to the NDME interface can be done through System Console totally in parallel while the Nios controller is also being used.
The NDME interface can be used for advanced debugging and reporting (see further) .
The major advantage of having the NDME interface is that it allows to run directly the Transceiver Toolkit (see further).

## Slide 29: Timing Closure (Setup)
The design is fully constraint and has no timing violations
Compiled for 10AX115S2F45I1SG

## Slide 30: Timing Closure (Hold)
The design is fully constraint and has no timing violations
Compiled for 10AX115S2F45I1SG

## Slide 31: Nios II Control & Monitoring
The Nios II controller is used to control and monitor the design using the Nios II terminal.
  Display status signals
    Freq_Locked
    Lane Identifier
    Pll_locked
    Link Up
    XOFF Received
    DataLocked (combination of the 4 PrbsLocked and Countlocked)
    WordAligned, LaneAligned
    Effective Datarate
    Efficiency
  Control Serial Loopback on all lanes.
  Control XOFF.
  Generate single biterrors in the generated data (note that inserting an error will result in 4 errors being seen : one per lane.
  Displays the number of biterrors and the BER.

## Slide 32: Nios II Control & Monitoring
  Allows to start a continuous BER measurement with a controllable interval (default time interval is 2 seconds).
  Displays the time the test has been running.
  Displays the measured reference clock frequency (Measured with 100 Mhz reference clock during 1 second).
  Control the voltage output level, all 5 pre-emphasis levels and equalization levels of the lanes, on a per lane basis
  2D and 1D ODI measurement
  Measures the minimum and maximum latency
Access is through Nios SDK shell (see further)

## Slide 33: Nios 2 Output in Nios II SDK Shell
Status window

## Slide 34: Nios 2 Output in Nios II SDK Shell (with external passive QSFP+ Loopback module)
PMA settings used for the result on the right:

## Slide 35: Available commands

## Slide 36: Measuring Latency
Option ‘M’ is measuring the maximum latency across 1000 resets and provides a histogram of this maximum latency being measured. (this can only be in serial loopback or with an external loopback)).
As can be seen latency is on average only 29 parallel clock cycles which is 185.6 ns at 10.3125 Gbps.

## Slide 37: ODI Measurement
The program offers the option to measure both 2D Eye as well as 1D eye on the selected lane.
Time for every measurement point can be dynamically set (Default 1 ms per measurement point)
Statistics are being provided including BER depth of the measurement.
Note that this design is using NPHY with ODI acceleration enabled to increase the BER Depth

## Slide 38: 1-D ODI/Bathtub

## Slide 39: Board Setup
Connect USB Cable to CN1 (USB II -Blaster is on the board itself).
Using Onboard oscillator :
  Set CLK_SEL (SW5.1) dipswitch to ‘OSC’ : No need to reprogram the Si570 (Y3) as it already generates a 644.53125 Mhz clock by default.
Using External Clock :
  Set CLK_SEL (SW5.1) dipswitch to ‘SMA’ to select the external clock. Connect a 644.53125 Mhz external clock to the External clock inputs
Download ‘Devkit_Demo.sof’ to the 10AX115S2F45I1SG device using QII programmer or through Signaltap II.

## Slide 40: Running the software (Option 1)
This is when you want to run the software with the already provided .elf file :
  Start a Nios II command Shell (can be found in the Quartus installation (e.g. C:\quartus_20_4\nios2eds) and go to the directory where the run1.bsh file is located.
  Since 20.4 Nios II terminal is using WSL, a quick way to go to the selected directory is to copy the complete path using windows explorer and in the Nios 20.4 terminal you type cd "$(wslpath “ => then you paste the path you copied (using right mouse click) => and end with typing ")“
    e.g. cd "$(wslpath "C:\ALTERA\Reference_Designs\SUPERLITEII\Arria10\A10_SIBoard_SuperliteII_V4_4_Lanes_10Gbps_QSFP+\software\app\Arria10GX_Superlite")“
  Since the quartus archive is restored in windows the files need to be converted from Dos to Linux. To do so either use “dos2unix –k *” or run the provided .bsh file “./convert.bsh” (note option –k keeps the original date of the file intact).
  Type In The Following Command : “./run1.bsh” This will set the JtagSpeed to 16M ,downloads and starts the program.

## Slide 41: Rebuilding the software (Option 2)
In order to rebuild the software do the following (using QII 20.3 or later):
  Start a Nios II command Shell (can be found in the Quartus installation (e.g. C:\quartus_20_3\nios2eds) and go to the directory where the run1.bsh file is located.
  Since 20.4 Nios II terminal is using WSL, a quick way to go to the selected directory is to copy the complete path using windows explorer and in the Nios 20.4 terminal you type cd "$(wslpath “ => then you paste the path you copied (using right mouse click) => and end with typing ")“
    e.g. cd "$(wslpath "C:\ALTERA\Reference_Designs\SUPERLITEII\Arria10\A10_SIBoard_SuperliteII_V4_4_Lanes_10Gbps_QSFP+\software\app\Arria10GX_Superlite")“
  Since the quartus archive is restored in windows the files need to be converted from Dos to Linux. To do so either use “dos2unix –k *” or run the provided .bsh file “./convert.bsh” (note option –k keeps the original date of the file intact).
  Run ./create-this-app .This will compile the system libraries (in the bsp folder), compile the software code (main.c and a number of other .c files in this case) and produce a Nios II executable.
If you make any changes to the software you need to rebuild by typing “make” in the Nios II 20.3 shell (after having created the software a first time)
To run the software : type In The Following Command : “./run1.bsh” This will set the JtagSpeed to 16M and download the Nios II code to the FPGA and open up the terminal.

## Slide 42: Demonstration on the board
LED’s
  LED0 : TxPLL_Locked (Transceiver locked to reference clock
  LED1 : Rx_Freqlocked status of selected channel
  LED2 : WordAligned
  LED3 : LaneAligned
  LED4 : LinkUp
  LED5 : Locked (CountLocked and all PRBSLocked signal asserted)
  LED6: Link OK : Locked + No biterrors
  LED7 : XOFF Received

## Slide 43: Signaltap II Debug Example
The design contains a number of signaltap instances, each clocked by it’s own clock.
Signaltap II acquisition can be done simultaneously with Nios II control.

## Slide 44: Use of NDME (Optional)
To access the NDME, open the System Console.
There is a sample script in the scripts folder which has a couple of useful debug procedures.
It can be started through “source ttk_helper.tcl” and provides a list of procedures available and the syntax to use.

## Slide 45: Using TTK_Helper.tcl script
When the system console is open you can source the ttk_helper.tcl script located in the scripts folder. This script contains a number of useful routines for advanced debug and setup.
A particular interesting procedure is one which set generator and checker to PRBS-31 and starts the tests.
To run this prodedure run : “start_check_prbs31”
See the attached file for an overview of available procedures. Including functions to do reverse serial loopback, polarity inversion, calibration, enabling, disabling dfe etc.

## Slide 46: Using Transceiver Toolkit (Optional)
To start the A10 Toolkit simply start it by clicking on it when opening the system console.
So you can e.g. run an autosweep using TTK to find optimum settings and when you go back to the original design (after pressing ‘1’) all the PMA settings as entered in the TTK will be kept and used. Vice Versa all PMA settings done through the Nios design will also be read out automatically and used by the TTK.
Note that if PRBS tests have been started during the testing and even if stopped and the Toolkit is closed the original functionality is lost and you need to download the SOF file again. If you do not enable the PRBS testing this is not a problem.

## Slide 47: Using Transceiver Toolkit (Optional)

## Slide 48: Using Transceiver Toolkit (Optional)

## Slide 49: TestBench
First steps :
Open a Nios II 20.4 Command Shell and go to the simulation directory (see section “Running the software” on how to change the directory in an easy way)
Run dos2unix –k *
Run ./create_simscript.bsh (for Windows)
On linux use ./create_simscript_arc.bsh (for ARC/Linux environments) instead.
This will create the necessary simulation scripts to match your own environment.
When using Modelsim SE (or PE) or Questasim (tested with QuestaSim 10.1c)
  Change directory to simulation/mentor and next run ‘Sim.do’ do compile and simulate everything (when there are no libraries yet)
  Run ‘Resim.do’ when libraries already exist to re-compile only the design files and simulate the testbench
The simulation files can be found in the ‘simulation’ and ‘simulation/mentor’ directory
After LinkUp has been achieved the testbench will also insert 2 errors (each resulting in 4 biterrors) which are reported by the testbench.

## Slide 50: Deliverables
Quartus 20.4 B72 archive which contains the demo design files, the software source files, ttk_helper.tcl scripts and the testbench files.
The testbenches can be found after restoring the archive: <restored_project>/simulation
The software source files can be found after restoring the archive in the <restored_project>/software/app and <restored_project>/software/bsp folders/
The software executables.
SOF File.
ttk_helper.tcl file in the /scripts folder
This document.

## Slide 51: Status & Revision
V20.4
  Migrated all IP to 20.4
  Updated software and ODI measurement to the latest implementations.
  Modified transceiver file to support additional logic to enable ODI acceleration.

## Slide 52: Status & Revision
V20.3 : November 3rd 2020
  Major update to the core (see initial slides for details on the changes made)
  Succesfully tested with external QSFP+ loopback module
  Succesfully tested with S10 TX Superlite II V4 design using 1 meter DAC
V20.2
  Migrated all IP to 20.2
  Updated tx_ratematcher_control module to allow LinkUp status during the “training stage” so that when no data is being sent when the design is brought up (data_in_valid de-asserted) the link can reach succesful LinkUp and also the training data is not being “flagged” as valid data (bug).
  Updated rx_path_deskew to handle that training data is now sent as all “control” characters.
V16.1.0 : Initial release
  Succesfully tested with QSFP+ optical loopback module installed.

## Slide 53: Feedback and/or Questions?
Peter Schepers (peter.schepers@intel.com )
+32 495 57 32 22