## Slide 1: Stratix10 GX ‘SuperLite II V4’ Demo Design V20.3 for the Stratix10 GX SI Board (H-Tile PRODUCTION) 8 Lanes @ 12.5 Gbps routed to the QSFP28 modules
Peter Schepers
Technology Specialist FAE High Speed Interfaces
November 26th , 2020

## Slide 2: Introduction & Motivation
This design illustrates how to use the Superlite II V4 concept on Stratix 10 GX
The V4 version of Superlite II is based on the V2+V3 version.
The V2 version uses a valid signal in combination with the transmit data and there is also a ready signal provided which can potentially halt the transmit traffic for a short interval (based on filling level of Transmit FIFO). This interface is equivalent to the Avalon Streaming Interface.
The V3 version adds additional functionality :
  Link information is exchanged between the local and remote side and results in a LinkUp when both local and remote side are aligned.
  XOFF is used in order to allow for backpressure or Flow Control: ask remote side to stop sending traffic (when local side e.g. is not capable of receiving the data).
  Because of the exchanges between local and remote side the protocol is now a fully bidirectional protocol (V1 and V2 versions could be used fully unidirectional)
  This specific version is using 2 instances of the Superlite II V4 demo, each with 4 lanes running at 12.5 Gbps and each connected to the QSFP28 module. Using DAC or Fiber Optic connection a full system test can be done between the 2 modules, illustrating link-up, reset behaviour etc. In this case a lane swap is natively present to demonstrate the V4 capability.

## Slide 3: Introduction & Motivation
  The V4 version is the version where transmit datapath is clocked with a single clock derived from the transceiver. This simplifies the Tx statemachine and FIFO implementation and has a significant reduction of the latency.
  Additional features added in this latest V4 version :
Insertion and detection of Lane Identification: each lane has it’s own unique identifier. So if lane swap or lane re-ordering occurs the information received in terms of lane identification allows to automatically recreate the original data pattern. This helps in not having to worry about how the lanes are routed in layout or how cables are connected.
Added GENERIC parameter SIMPLEX which when set to true does not perform handshaking with the remote side and allows SIMPLEX operation (even when using Duplex transceiver). When parameter SIMPLEX is set to true, Linkup will be declared when LaneAligned is achieved locally.
Simplified exchange of control characters for flow control.
Tested interoperability with equivalent Superlite II V4 versions on S10TX (E-tile) and S10 GX (H-tile).
Latency measurement is inherently part of the protocol now.

## Slide 4: How to use Superlite II V4 in Packet mode ?
  By nature the Superlite II V4 is using streaming data (Avalon streaming based) so not framed or packetized . One could however support also a framed mode (or packet mode) by using one of the lanes to transport the packet related information (SOP, EOP, etc) . This does require an additional lane to provide the packet overhead information. This concept has been succesfully implemented on Stratix V GX (with 11 lanes) and can easily be repeated on Stratix10 (with higher rates and including KR-FEC).

## Slide 5: ‘SuperLite II V4’ Concept

## Slide 6: ‘SuperLite II V4’ Concept
Transport data from point A to point B as simple as possible multiple bidirectional serial links. Note that the number of lanes in each direction do not have to be equal.
V3 version of the protocol exchanges information between local and return side (handshaking) as well as XON/XOFF control (backpressure)
On the transmit side data will only be written in the FIFO when the valid signal is asserted, the fifo also can issue a backpressure signal (indicated by the ‘ready’ signal to indicate if data can be transmitted. This is equivalent to the Avalon Streaming interface.
When XOFF is received from the remote side, all traffic will be halted on the local side (link remains up though).
The transmit datapath is entirely clocked on the clock derived from the transceiver (transmitted line rate/66).
On the receive side it will be based on the recovered clock (received line rate/66) with data valid. The combination of data valid with the recovered clock is frequency locked to the clock used at the transmit side.
Uses 64/66 Encoding in combination with scrambling.
Multiple lanes are bonded, there is no real limit on the number of lanes that can be used, apart from potential limitations to compile very large number of lanes. Typically 4 or 10 lanes will be used. Also a single lane is possible.
For word alignment and lane alignment idle characters and alignment characters will be sent at regular intervals

## Slide 7: ‘Superlite II V4’ Concept (continued)
The Superlite II V4 TX module will automatically pause Tx user data if needed to insert idle and alignment characters and will also pause Tx user data based on the “ready” received from the Native PHY (as it is working in overspeed). So the userdata needs to be able to immediately stop sending traffic. If this is not possible one can add an additional FIFO with a slower running write clock.
User data is always 64 bit per lane because of the 64b66b encoding.
Efficiency is calculated as (Read_Length)/(Read_Length + Idle_Length) * 64/66, so e.g. for the parameters used in the demo design : 1056/(1056+7) * 64/66 = 96.33%. By increasing the Read_Length the efficiency/net rate can be increased.

## Slide 8: SuperLite II V4 2x4 lane Demo Design
Goals :
  Demonstrate the Superlite II V4 concept on Stratix10 GX
    Use Stratix10 GX Signal Integrity board as platform for demonstration.
      Uses 2 Superlite II V4 demo instances (each with their own packet generator and checker). Each instance (or “phy”) is connected to the QSFP28 module
      Full system validation can be done using either a DAC cable (various length) or Fiber Optic connection using QSFP+ modules (in this case the datarate should be run at the Fiber Optics rate (typically 10.3125 Gbps)
      Due to the layout of the RevD board one of the QSFP28 lane assignments are swapped making it ideal to test the V4 functionality.
    Line rate in this demo is 12.5Gbps per lane but could be go all the way up to 28.3 Gbps (See the 25.78125 Gbps demo design that is also available)
    4 lanes will be used for each phy, therefore aggregate line rate is 50 Gbps per phy
    User data width is 256-bits (64 bits per lane) per phy
    Actual throughput depends on the configured “read time” and “idle time” parameters. In the demo the “read time” is 1056 clock cycles and “idle time” is 7 clock cycles but these can be easily changed. The “read time” would normally be set at a higher value like e.g. 67584 clock cycles in order to increase the efficiency.
    The user data is generated based on the 189.3939 Mhz clock generated by the Native PHY (data rate divided by 66). As it receives backpressures from the Superlite II V4 Tx module the data will be halted at specific times
    To create the 256 bit user data in each phy a combination of different counterpatterns and prbspatterns are used across the 4 lanes of each phy

## Slide 9: Goals (continued)
Goals :
  Use Reconfiguration Management Interface for Native PHY and LC PLL through QSYS system.
  Through NDME Transceiver Toolkit support is automatically available.
  Use Nios II processor as controller/monitor
  Allows to perform ODI Measurement from within the Nios command shell, measuring both 2D eye as well as bathtub curve on the selected lane and provide statistics (Eye height, width etc).
  Includes PMA sweep functionality
  Includes Testbench
  Supports background calibration.
  I2C support for the QSFP28 modules with automatic readout of capabilities.
  software executable (.elf) is part of the program memory.

## Slide 10: ‘SuperLiteII V4’ Resources (one phy)
SuperliteII V4 TxRx Module Resources 4 lanes at 12.5 Gbps.
Note : A large % of the resources is taken by the additional logic enabled in the Native PHY for debug purposes (like NDME etc) This is additional debug logic that is not required for a full design).
  ~ 2500 ALUT’s
  ~ 1700 ALM’s (needed)
  ~ 2450 Dedicated logic registers
  7 M20K’s

## Slide 12: ‘txrx_pcs_64b66b’ Detailed blockdiagram

## Slide 13: Tx Path
A datastream is generated at a clock of 189.3939 Mhz @ 256 bit when DataIn_ready is high. The datapattern is a combination of 4 60-bit Prbs-23 (each with their own starting value) and one 16-bit counterpattern.
  The 16-bit counterpattern is spread across the 4 lanes, 4 bits per lane. This is to make sure any deskew on the lanes would be immediately spotted.
Since idle and alignment characters have to be inserted at regular intervals the data stream will be halted at regular intervals in order to insert the required idle and alignment characters. This is indicated by the Superlite II TX module by the DataIn_ready signal.
In case XOFF is received from the Remote side the DataIn_Ready signal will be low to avoid any traffic being sent.
Single biterrors can be inserted using inserterror input. As there is one PRBSGenerator per lane, the biterror insert will produce 4 bit-errors at a time in fact.
This data is presented to the Superlite II Tx Module
The data is written into the TxFifo using the 189.3939 Mhz as write clock and using the DataIn_Valid as write-enable.
The read clock for the TxFifo is the same 189.3939 Mhz clock which is driven from the tx_clkout of the transceiver PHY
During the intervals that readenable is deactivated, idle characters and the alignment characters will be inserted in the datastream which is fed to the 64b66b encoder blocks.

## Slide 14: Tx Path (continued)
The 64b66 encoding is very straightforward : bits 65..64 are set to “10” for control data and “01” for data (so neutral disparity)
In terms of idle character a value of “1C1C….1CBC” is being used. The alignment character is sent as the last control character. The lower 16 bits of this control word (at the alignment position) encodes the status of the link in addition to the alignment indication.
If no local alignment has been found : the last control word sent is “..7C7C”
If local wordalignment has been found : the last control word sent is “..FD7C”
If XOFF is being sent to the remote side : the last control word sent is “..5C7C”
Lane Alignment coding (B<i> is the byte)
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
Lane Identity | Latency Count Tx | 7C | 7C | 7C | 7C | FD/5C/7C | 7C

## Slide 15: Tx Path (continued)
The resulting 66-bit is sent to the Native PHY where the scrambler is enabled and the gearbox converts it from 66-bit to 64-bits PMA
In order to make sure there is DC balance and enough transitions present on the serial links a selfsynchronizing scrambler is used, in this implementation the scrambler of the Enhanced PCS is used. The scrambler will scramble only the 64 databits (the framing bits on bits [65..64] are not scrambled since they are required for the framing. The polynomial used for the scrambler is 1 + x^39 + x^58 according to the IEEE.
Finally the data is serialized in the Native PHY (using 64-bit serializer) and sent out as serial datastreams (12.5 Gbps per lane).

## Slide 16: Rx Path
After deserialization the data is presented to the Rx Block Synchronizer inside the Native PHY where it will automatically align on the incoming valid 66 bit words. The descrambling is also done inside the Enhanced PCS.
This is all happening on all lanes at the same time and everything is clocked based on the recovered clock of channel 0. The phasecompensation FIFOs inside the Enhanced PCS will be used to make sure lanes 1 to 4 have the right phaserelationship. Note that the recovered clock on lanes 1 to 4 are the same frequency as lane 0 but have a different phase relationship, hence the need for the phasecompensation FIFOs.

## Slide 17: Rx Path (continued)
Based on the position of the alignment word, the delay for each lane is measured, the statemachine inside the Rx_path_deskew module will use the information of that measured delay to control a special Rx FIFO signal “rx_fifo_rd_en” on all RxFIFO’s inside the Native PHY to deskew all the lanes.
Once lane alignment is achieved the 256-bit combined data in addition with a data valid signal will be sent to the data verifier.
Here PRBS and counterverification will take place and single biterrors will be counted.
Prbslocked is asserted when 128 consecutive valid Prbs-23 60-bit words have been received on each of the lanes and de-asserted when 128 consecutive non-valid Prbs-23 60-bit words have been received.
Countlocked is asserted when 128 consecutive valid 16-bit counter words have been received on the parts of the lanes they were received.
There are 4 60 bit PRBS Verifiers (one for every lane) and 1 16-bit CountVerifiers to validate the 256 bit data.

## Slide 18: Rx Path (continued)
The V3 version adds an additional Rx State machine to the logic to determine the local Rx state and it depends on the incoming “alignment” control word
If last control word received is “…FD7C” it means the remote side has reached Wordalignment, if local side also has reached wordalignment this results in Linkup to be asserted, indicating that both sides are up and running. This can be used as the trigger to sent data across e.g.
If last control word received is “…5C7C” it means an XOFF has been received from the remote side, this will be forwarded to the local transmitter to stop generating traffic on the local side.
(See Flow chart on next slide for more details)

## Slide 19: Control Characters used in combination with XOFF

## Slide 20: Transceiver Configuration (1/6)
A 4 lanes Duplex Native PHY is selected using 1_V and GX channels. Using Enhanced PCS, a datarate of 12.5 Gbps from a 625 Mhz referenceclock. PCS/PMA interface width is 40 and FPGA fabric/Enhanced PCS width is 66. Important : make sure the low latency mode is enabled.

## Slide 21: Transceiver Configuration (2/6)
In order to use the Rx FIFO for deskewing the lanes the optional signal “rx_enh_fifo_rd_en” must be enabled as well as the rx_fifo_pempty port, the other signals are used for debug only.
RX PCS-Core Interface FIFO mode should be set to “Phase Compensation-Basic”, notice also the threshold levels being used.

## Slide 22: Transceiver Configuration (3/6)
Tx Scrambler (with Seed pattern shown below) and Rx Descrambler should be enabled.
Block Sync should be enabled.

## Slide 23: Transceiver Configuration (4/6)
It is very important to enable the “Enable Tx Data Valid Gen Manual Setting” and set it to “enable”, otherwise the gearbox functionality will not operate correctly and the design will not be functional.

## Slide 24: Transceiver Configuration (5/6)
Enable both tx_clkout2 and rx_clkout2 and use the pma_div_clkout with 33 division factor, this will generate the tx_clkout and rx_clkout at datarate/66 to the core logic.

## Slide 25: Transceiver Configuration (6/6)
To enable a full set of debug capabilities (including UTK functionality) all the options as shown below are enabled. Note that in a final design these are not all mandatory and can be disabled to save resources. Analog PMA settings will be set by the software during operation.

## Slide 26: Stratix 10 H-Tile Transceiver ATX PLL

## Slide 27: Transceiver Reset Controller
Note that the duration of the rx_digitalreset has been extended from 5 us (default) to 50 ms. The reason is that for lossy channels (like 5 meter of DAC cable) the adaptation of CTLE/VGA/EQ takes a relative long time to converge, PRBS verifiers need to be kept in reset until the adaptation has finished.
(Note that 50 ms might be an overkill, a test with 5 ms was not enough so the ideal value will be somewhere in between).

## Slide 28: Reconfig Management Interface.
The Native PHY as well as the ATX PLL have an Avalon MM Interface which allow full control of the register space of the transceiver and the ATX PLL.
The AVMM used for the Native PHY is using shared addressing for all channels and provides one interface to the .QSYS system.
The AVMM used for the ATX PLL provides another separate interface to the .QSYS system.
This design is using a QSYS system which transparently maps the AMM interfaces to the Native PHY and the ATX PLL.
The component created for this in QSYS is called “reconfig_mgmt” and the reconfig_mgmt_hw.tcl file included in the project describes it’s implementation.
You can verify it’s content by editing the reconfig_mgmt component.

## Slide 29: NDME Interface
In addition to the AVMM interface the Native PHY also enables the NDME interface (Native PHY Debug Master Endpoint) which can also be accessed through the Qsys system due to the addition of the jtag_debug_module.
Access to the NDME interface can be done through System Console totally in parallel while the Nios controller is also being used.
The NDME interface can be used for advanced debugging and reporting (see further) .
The major advantage of having the NDME interface is that it allows to run directly the Transceiver Toolkit (see further).

## Slide 30: Timing Closure (Setup)
The design is fully constraint (with signaltap enabled). Compiled for 1SG280HU2F50E2VG

## Slide 31: Timing Closure (Hold)
The design is fully constraint (with signaltap enabled). Compiled for 1SG280HU2F50E2VG

## Slide 32: Nios II Control & Monitoring
The Nios II controller is used to control and monitor the design using the Nios II terminal.
  Display status signals
    Freq_Locked
    Lane Identifier
    Pll_locked
    Link Up
    XOFF Received
    DataLocked (combination of the 4 PrbsLocked and Countlocked)
    WordAligned, LaneAligned
    Effective Datarate
    Efficiency
  Control Serial Loopback on all lanes.
  Control XOFF.
  Generate single biterrors in the generated data (note that inserting an error will result in 4 errors being seen : one per lane.
  Displays the number of biterrors and the BER.

## Slide 33: Nios II Control & Monitoring
  Allows to start a continuous BER measurement with a controllable interval (default time interval is 2 seconds).
  Displays the time the test has been running.
  Allows to perform a full 2D and 1D ODI measurement on the selected channel.
  Allows to find the optimum PMA settings (AC gain, EQ Gain, VGA gain, VOD, Pre-emphasis, CTLE Offset coefficients) using PMA sweep function. (Option ‘U’)
  Displays the measured reference clock frequency (Measured with 100 Mhz reference clock during 1 second).
  Measures the maximum latency (only when looped back to itself)
  Dumps I2C information of connected modules and cables like Vendor, part number, cable length, temperature of the module.
  Allows to dump the I2C page Lower page and Page 00h registers of the selected module/cable
Access is through Nios SDK shell (see further)

## Slide 34: Nios 2 Output in Nios II SDK Shell (5 meter DAC)

## Slide 35: Status and PMA settings PHY 0 (5 meter DAC)

## Slide 36: Status and PMA settings PHY 1 (5 meter DAC)

## Slide 37: Sweep PMA settings
Screenshot below shows a new option (‘u’) that allows to sweep the PMA settings and perform BER and EyeQ measurement for every step. At the end of the sweep you will get 3 metrics (3 FOM) : one for the best BER, one for the largest Eye (if any) and one for most symmetrical vertical eye. It is up to the user to manually enter which setting to use, the user has also the option to select any setting.
Since the setup requires by default a connection between the 2 QSFP modules, when a sweep is done the Tx channel is automatically taken from the corresponding phy.

## Slide 38: Sweep PMA settings Example
Sweeping Pretap 1 on channel 0 (which means Phy 1 Tx 0 and Phy 0 Rx 3 (because of the lane swap, this is automatically taken into account based on the Lane Identifier)

## Slide 39: Available commands

## Slide 40: ODI Measurement
Using option ‘o’ a full 2D and 1D eye measurement will be done on the selected channel. To set the runtime (i.e. the amount of bits to be tested at every testpoint) you can change it using option ‘g’. By default the runtime is set to 2^16 which gives the fastest eye measurement. All relevant statistics about the eye measurement are also provided
See next slide for example which shows the 2D eye after 5 meter of DAC cable at 12.5 Gbps using the default runtime setting. As can be seen the eye measurement takes ~11 seconds to complete with the default runtime setting of 2^16.

## Slide 41: 2D Measurement
The eye captured on the right is Phy0 channel 0 (using 5 meter DAC cable) at 12.5 Gbps

## Slide 42: Bathtub measurement
The picture below shows the 1D or “bathtub” curve.
Note that this is measured at the vertical offset determined from the 2D measurement (in the example below this is at 1).

## Slide 43: 2D Eye dump
After the ODI measurement is complete, you are being asked whether you want to dump the 2D array as text (comma separated). If you press ‘d’ this will be done.
(you can have as many dumps made as you want).
If you quit the Nios application (by pressing CTRL+C) the output.log file that is generated will contain these 2D arrays and in order to extract only the eye information from this, you need to run the command “./csv.bsh”.
This will generate a file called eye.csv which contains all the captured eye information and header information.
Once you have generated such an eye.csv file you can further analyse it by starting the adv_link_analyzer_data_viewer.exe (included in the deliverable).
In this tool
select the BER noise floor (for default ODI runlength, choose a value of 13)
Click on CSV and open the generated eye.csv file.
The tool will parse the eye.csv file and displays all captured eyes and provides a full analysis (EW ,EH at selected BER, bathtub curves, jitter at BER etc.)
(see snapshot on next page)

## Slide 45: Option ‘y’ to measure all 2D eyes at once
If you type ‘y’ in the Nios console it will automatically perform a 2D eye measurement for all the channels in the design (if a design is not locked no measurement will be done).
This is a very fast way of capturing all eyes which can be displayed using the Advanced Link Analyzer Data viewer (the snapshot on previous page shows this after having captured all eyes).
The total measurement time for capturing all eyes only takes less than 90 seconds (8 channels)

## Slide 46: Measuring Latency
Option ‘M’ is measuring the maximum latency across 1000 resets and provides a histogram of this maximum latency being measured. (this can only be measured when qsfp_to_qsfp is set to 0 in the main.c or serial loopback is used).
As can be seen maximum latency is on average 34 parallel clock cycles which is 179 ns (measured with serial loopback)

## Slide 47: Board setup
Connect QSFP DAC cable or Optical Fiber connections between the 2 QSFP+ modules
Connect USB Cable to CN1 in order to use onboard USB-Blaster II.
Program the clocks Using the clock control GUI as shown on the next slide
Download ‘Devkit_Demo.sof’ to the 1SG280HU2F50E2VG device using QII 20.3 programmer.

## Slide 48: Clock control

## Slide 49: Running the software (Option 1)
This is when you want to run the software available inside the program memory, Do the following :
  Start a Nios II command Shell (can be found in the Quartus installation (e.g. C:\quartus_20_3\nios2eds) and go to the directory where the .start.bsh file is located.
  Since 20.3 Nios II terminal is using WSL, a quick way to go to the selected directory is to copy the complete path using windows explorer and in the Nios 20.3 terminal you type cd "$(wslpath “ => then you paste the path you copied (using right mouse click) => and end with typing ")“
    e.g. cd "$(wslpath "C:\ALTERA\Reference_Designs\SUPERLITEII\Stratix10\S10_SIBoard_SuperliteII_V4_8_Lanes_26G_Prod\software\app\Stratix10GX_xCh")“
  Since the quartus archive is restored in windows the files need to be converted from Dos to Linux. To do so either use “dos2unix –k *” or run the provided .bsh file “./convert.bsh” (note option –k keeps the original date of the file intact).
  Type In The Following Command : “./start.bsh” This will set the JtagSpeed to 16M and start the Nios II code embedded inside the main program memory.

## Slide 50: Rebuilding the software (Option 2)
In order to rebuild the software do the following (using QII 20.3 or later):
(Note that if you use 20.3 you need to install patch 0.09 to remove issues with Windows 10 WSL)
Start a Nios II 20.3 Command Shell
  go to the ../software/app/Stratix10GX_xCh directory (which is part of the archive) using the method descriped on the previous slide
  Run the bash file ./convert.bsh (this will also convert the files in the bsp folder)
  Run ./create-this-app .This will compile the system libraries (in the bsp folder), compile the software code (main.c and a number of other .c files in this case) and produce a Nios II executable.
If you make any changes to the software you need to rebuild by typing “make” in the Nios II 20.3 shell (after having created the software a first time)
To run the software : type In The Following Command : “./run1.bsh” This will set the JtagSpeed to 16M and download the Nios II code to the FPGA and open up the terminal.

## Slide 51: Use of NDME (Optional)
To access the NDME, open the System Console.
From here you have access to all AVMM registers from the Native PHY as well as the ATX PLL’s
See next pages for more information.

## Slide 52: Use of NDME (Optional)
To access the NDME, open the System Console.
From here you have access to all AVMM registers from the Native PHY as well as the ATX PLL
See next pages for more information.

## Slide 53: Transceiver Toolkit and ttk_helper_s10.tcl script
When you open the TTK you will see already all channels being running and counting errors as this has been started already after downloading the Nios.
When the system console is open you can also source the ttk_helper_s10.tcl script located in the scripts folder. This script contains a number of useful routines for advanced debug and setup.
See the attached file for an overview of available procedures. Including functions to do reverse serial loopback, polarity inversion, calibration etc.

## Slide 54: Identification of Native PHY and PLL’s
When the script is sourced it also lists all the Native PHY’s, ATX PLL’s and fPLL that have NDME enabled and this information can be used to identify which particular PHY corresponds to the RTL instantiated PHY (or PLL).

## Slide 55: Using Transceiver Toolkit (Optional)
To start the H-Tile Toolkit simply start it by clicking on it when opening the system console.
So you can e.g. run an autosweep using TTK to find optimum settings and when you go back to the original design (after pressing ‘1’) all the PMA settings as entered in the TTK will be kept and used. Vice Versa all PMA settings done through the Nios design will also be read out automatically and used by the TTK.
Note that if Prbs tests have been started during the testing and even if stopped and the Toolkit is closed the original functionality is lost and you need to download the SOF file again. If you do not enable the PRBS testing this is not a problem.

## Slide 56: H-Tile Toolkit screenshot

## Slide 57: H-Tile Toolkit screenshot

## Slide 58: EyeQ Measurement (Ch0, after 5 of DAC cable (25.8Gbps)

## Slide 59: Demonstration on the board
LED’s
  LED0 : TxPLL_Locked (Transceiver locked to reference clock
  LED1 : Rx_Freqlocked status of selected channel
  LED2 : WordAligned
  LED3 : LaneAligned
  LED4 : LinkUp
  LED5 : Locked (CountLocked and all PRBSLocked signal asserted)
  LED6: Link OK : Locked + No biterrors
  LED7 : XOFF Received

## Slide 60: Signaltap II Debug Example
The design contains a number of signaltap instances, each clocked by it’s own clock.
Signaltap II acquisition can be done simultaneously with Nios II control.

## Slide 61: TestBench
First steps :
Open a Nios II 20.3 Command Shell and go to the simulation directory (see section “Running the software” on how to change the directory in an easy way)
Run dos2unix –k *
Run ./create_simscript.bsh (for Windows)
On linux use ./create_simscript_arc.bsh (for ARC/Linux environments) instead.
This will create the necessary simulation scripts to match your own environment.
When using Modelsim SE (or PE) or Questasim (tested with QuestaSim 10.5c)
  Go to the folder ../simulation/mentor
  Run ‘Sim.do’ do compile and simulate everything (when there are no libraries yet)
  Run ‘Resim.do’ when libraries already exist to re-compile only the design files and simulate the testbench
The simulation files can be found in the ‘simulation/mentor’ directory
After lane alignement has been achieved the testbench will also insert 2 errors (each resulting in 4 biterrors) which are reported by the testbench.
Note that the testbench contains 2 instances of the Superlite II design to mimic the hardware setup and to validate the system implementation and lane swapping between the 2 is done differently

## Slide 62: Deliverables
Quartus 20.3 archive (B158) which contains the demo design files, the software source files, ttk_helper_s10.tcl scripts and the testbench files.
The testbenches can be found after restoring the archive: <restored_project>/simulation
The software source files can be found after restoring the archive in the <restored_project>/software/app and <restored_project>/software/bsp folders/
The software executables.
SOF File.
ttk_helper_s10.tcl file in the /scripts folder
This document.

## Slide 63: Status & Revision
V20.3 : November 26th 2020
  Initial release of the 12.5Gpbs version which is based on the 25.8 Gbps version released earlier but this version has lower latency as it allows to use low latency mode and uses embedded features inside the enhanced PCS : scrambler/descrambler and block synchronization.
  Succesfully tested with 5 meter DAC cable.

## Slide 64: Feedback and/or Questions?
Peter Schepers (peter.schepers@intel.com )
+32 495 57 32 22