## Slide 1: Stratix10 TX DYNAMIC RECONFIGURATION DEMO DESIGN : RECONFIGURE FROM/to - RSFEC Fractured NRZ/PAM4 (528,514) [Reconfigurable RATE] - RSFEC Fractured NRZ/PAM4 (544,514) [Reconfigurable RATE] - KPFEC AGGREGATE PAM4 (544,514) [Reconfigurable RATE] - PMA DIRECT NRZ (4 lanes at 25.7812 Gbps or reconfigurable Rate) - PMA Direct PAM4 (2 lanes at 53.125 Gbps or reconfigurable rate) - (new) Independent RSFEC FRACTURED Lane to PMA direct at configurable rate + Soft PRBS + OPTIONAL SCRAMBLING + SOFT ADAPT IP + STRESS TESTS Routed to QSFP-DD 2x1 Stratix 10 TX Signal Integrity Board (PRODUCTION) V21.1
Peter Schepers
Technology Specialist FAE High Speed Interfaces
June 7th, 2021

## Slide 2: Introduction & Motivation
This design instantiates 2 PHY’s configured by default with RSFEC enabled in fractured mode (RS528,514) each capable of doing >100G throughput using soft PRBS. Each Lane can operate up to 28.9 Gbps NRZ or PAM4.
This particular demo design allows the following dynamic reconfigurations :
RSFEC Fractured NRZ/PAM4 (528,514) with reconfigurable rate
RSFEC Fractured NRZ/PAM4 (544,514) with reconfigurable rate
KPFEC AGGREGATE PAM4 (544,514) with reconfigurable rate
PMA DIRECT NRZ (4 lanes up to 28.9 Gbps) with reconfigurable rate
PMA Direct PAM4 (2 lanes up to 53.125 Gbps) with reconfigurable rate
NEW : Reconfigure lane 1-3 from RSFEC to PMA direct with reconfigurable datarate (1.25 Gbps-28.9 Gbps)
NEW : when in PMA direct NRZ mode : reconfigure lane 0-3 to any reconfigurable datarate (1.25 Gbps -28.9 Gbps)

## Slide 3: Introduction & Motivation (continued)
In all cases the amount of virtual channels is 4 and the datapath is 256 bits.
SoftPRBS data generators and checkers are being used to test the traffic. Generators and checkers operate on 64 bit datapath, except for the PMA direct PAM4 configuration in which case 128 Bit Generators and checkers are used.
Scrambling of the userdata can be dynamically turned on/off when using non-PMA direct modes. Scrambling is not required when using PRBS data but with regular data it should always be enabled.
For the 64-bit PRBS generation each instance will use a different seed value in order to avoid the same pattern (including long runs and zeros on the 256 bit datapath).
To control the RSFEC additional control signals are being generated in combination with the soft PRBS data.
Soft Adapt IP : This design implements in every PHY instance a QSYS system with a small Nios and embedded RAM. This QSYS system allows to run the adaptation search algorithm independently while the main program is running. Additional arbitration and a mutex is added so that at any point of time only one “master” can access the transceiver registers.

## Slide 4: DPRIO RSFEC/KPFEC Soft PRBS/Dynamic Reconfig with Adapt SIP Demo Design
  Demonstrate the dynamic reconfiguration flexibility on Stratix10 TX using Native PHY
    Use Stratix10 TX Signal Integrity board as platform for demonstration.
      Uses 2 Native PHY’s with RSFEC in fractured mode (default) with each 4 physical lanes connected to QSFP-DD 2x1 (upper and bottom). Design starts by default in 25.78125 Gbps per lane with RSFEC Fractured enabled
      Since RSFEC in fractured mode can only be implemented with Reset controller bypass mode, the design controls all the relevant reset signals required through software implementation (As well in the testbench)
      Each phy is clocked by it’s own referenceclock (to have ppm differences)
    Implements dynamic reconfiguration (From/To the following configurations)
    RSFEC Fractured NRZ/PAM4 (528,514) (line rate is 25.78125 Gbps from 156.25 Mhz clock (x165) or reconfigurable to any rate)
    RSFEC Fractured NRZ/PAM4 (544,514) (line rate is 26.5625 Gbps from 156.25 Mhz clock (x170) or reconfigurable to any rate)
    KPFEC AGGREGATE PAM4 (544,514) (line rate is 53.125 Gbps from 156.25 Mhz clock (x170x2) or reconfigurable to any rate)
    PMA Direct NRZ (line rate is 25.78125 Gbps from 156.25 Mhz clock (x165) or reconfigurable to any rate)
    PMA Direct PAM4 (line rate is 53.125 Gbps from 156.25 Mhz clock (x170x2) or reconfigurable to any rate)
    NEW : Reconfigure lane 1-3 from RSFEC to PMA direct (line rate is (tx_clk_divider (configurable) x refclk frequency)
    NEW : when in PMA direct NRZ mode : reconfigure lane 0-3 to any reconfigurable datarate (line rate is (tx_clk_divider (configurable) x refclk frequency)
    User data width is 64-bits per virtual lane/for PMA Direct PAM4 user data-width is 128-bit.

## Slide 5: Goals (continued)
    The user data is generated based on the datarate/64 clock generated by the Native PHY.
    Uses QSYS system per Native PHY to run the adaptation search independently, referred to as ADAPT_SIP
  I2C support is available to the QSFP-DD modules with automatic readout of capabilities.
  Support for PMA configuration options (10G,28G LR, 28G VSR, 56G LR, 56G VSR)
  Support for3 different effort levels for iADP which can reduce iADP time drastically.
  Support for LPM (Low Power Mode of the transceivers : reduces power consumption)
  Support for Reverse Parallel Loopback
  Uses Release Reset IP (recommended for all S10 designs from 19.1 onwards)
  Support for Rx Termination settings based on the presence of external AC coupling capacitors.
  Design uses a Qsys system with Nios II Processor to control the Native PHY’s in the PHY and control all other logic (temperature measurement, I2C control, fan control etc.)
  To create the 2x4 64 bit user data 64-bit soft PRBS generators and 64-bit PRBS checkers are being used.
  Each 64-bit Prbs Generator will use a different seed to avoid the same pattern being sent on the 256 bit bus.
  For the PMA direct PAM4 : to create the 2x2 128 user data 128-bit soft PRBS generators and 128-bit PRBS checkers are being used.
  PrbsAlarm signal : the PrbsAlarm signal will be asserted when the PrbsLock will go down (due to external causes e.g. cable pull/plug in) and remain asserted until a reset errorcount or reset of the phy is being done. This allows to capture any events that could occur that could bring down a link for a period of time to keep track of this.

## Slide 6: Goals (continued)
  Scrambler/Descrambler can be dynamically enabled/disabled (except for the PMA direct modes). Each virtual lane has it’s own scrambler/descrambler. Scramblers/Descramblers used are self synchronizing as used by Ethernet IEEE interfaces with polynomial 1 + x^39 + x^58
  Additional control signals required for the RSFEC operation are also generated in the design.
  PRBS Patterns that can be configured are PRBS-7, PRBS-9, PRBS15i, PRBS-23 and PRBS-31.
  Uses Reconfiguration Management Interfaces for the E-tile transceiver.
  Through NDME Universal Toolkit support is automatically available.
  Use Nios II processor as controller/monitor.
  Reports errorcount and calculates BER based on the received data.
  Includes Testbench for the 4 channel RSFEC Fractured configuration

## Slide 8: ADAPT_SIP Resources
  Below is a screenshot of the amount of resources being used by one ADAPT_SIP instance. Note that this can still be further optimized in memory footprint as printf is being used which has an impact on the resources. Those printf are not required for the functionality but from a demo point of view show what is going on currently in each ADAPT_SIP.
    ALMs : ~ 1500
    ALUTs : ~1900
    Dedicated Logic Registers : ~ 1500
    M20K : 101

## Slide 9: E-Tile Native PHY (TX PMA/RX PMA)

## Slide 10: E-Tile Native PHY (RSFEC)

## Slide 11: E-Tile Native PHY (Core Interface)

## Slide 12: E-Tile Native PHY (PMA Interface)

## Slide 13: E-Tile Native PHY (Dynamic Reconfiguration)

## Slide 14: Dynamic reconfiguration from Fractured to Aggregate (1/2)
  To dynamically reconfigure from the original RSFEC Fractured NPHY configuration to the PAM4 NPHY Aggregate configuration a similar design is generated which instantiates the PAM4 KPFEC configuration (see next slides for the details).
  In this design a dump of the transceiver registers is being done for channel 0 and channel 1 (which is special for the PAM4 case). These “dumps” are automatically captured using a .bsh script and converted into C include files (.h ) that contain each an integer array with the register information.
  The same is done for the original RSFEC fractured NPHY configuration (only channel 0 is required in this case)
  In the software itself the reconfiguration functions are implemented entirely as a c functions : reconfigure_to_rsfec_aggregate(int phy) and reconfigure_to_rsfec_fractured (int phy)
  The reconfiguration procedure starts by asserting the relevant resets and then streams in the data from the “dumped” configurations using function reconfigure_channel_dump (int phy, int channel,unsigned int dump[564])
  Important (as the phy’s use a different refclk input the refclk selection needs to be set correctly while streaming in the new file) This is being done in the reconfigure_channel_dump function. If the design is modified to use a different referenceclock input than in this demo design it needs to be modified accordignly.

## Slide 15: Dynamic reconfiguration from Fractured to Aggregate (2/2)
  The next step is to reconfigure the RSFEC to the required mode:
    For KPFEC Aggregate this means :
      Setting the RSFEC core to aggregate
      Set all EMIB Lanes to have TX Data with Deskew
      Specifies all channel to include in the deskew procedure
      Set the RSFEC to (544,514)
      Set the bit to control the Aggregate mode for the RTL design (this will generate the correct cadence required for aggregate amongst others)
    For RSFEC Fractured this means :
      Setting the RSFEC core to fractured
      Set all EMIB Lanes to have TX Data without Deskew
      Remove all channels from the deskew procedure
      Set the RSFEC to (528,514)
      Set the bit to control the Fractured mode for the RTL design (this will generate the correct cadence required for fractured amongst others)
    Next an analogue reset is being done after which all the relevant PMA settings are reprogrammed
    Finally the resets are being de-asserted and an iADP is being run.

## Slide 16: Special requirement for generating the NPHY in KPFEC aggregate mode
  The NPHY configuration for the KPFEC in aggregate mode currently does not allow to set the reset controller to bypass (which is the mode used for the RSFEC in fractured). In order to have the exact same implementation in terms of reset controller bypass however the NPHY needs to be generated in a similar way.
  This is achieved by the following modification in xcvr_kpfec.ip
  change parameters
  “enable_direct_reset_control” from value 0 to value 1
  “l_enable_direct_reset_control” from value 0 to value 1
  “l_enable_direct_reset_control_ports” from value 0 to value 1
  save the file and open the .ip file.
  For the details of the NPHY in KPFEC aggregate see the next slides (only differences with the fractured configuration are shown the rest is the same)

## Slide 17: E-Tile Native PHY KPFEC Aggregate (TX PMA/RX PMA)

## Slide 18: E-Tile Native PHY KPFEC Aggregate (RSFEC)

## Slide 19: E-Tile Native PHY KPFEC Aggregate (PMA Interface)

## Slide 20: Dynamic reconfiguration to PMA direct mode
  This is using the same approach as the other reconfiguration options, but this time using the “dump” from one channel from a Native PHY configuration which is streamed in followed by the required actions to bypass the RSFEC.
  Each PHY instance is instantiating 8 clock multiplexers (generated by logic) to select the right tx_coreclk and rx_coreclk for each of the lanes.
    Tx_coreclk(I) = Tx_clkout(I) when NRZ pma direct mode else Tx_Clkout(0)
    Rx_Coreclk(I) = Rx_clkout(I) when NRZ pma direct mode else Rx_Clkout(0) when PMA direct PAM4 else Tx_clkout(0) (FEC modes).
  Phase comp fifo’s are used on each of the lanes to accommodate for this additional clock crossings.
  In this configuration the recovered clock frequency is equal to the line rate instead of being 64/66 the line rate for the RSFEC configurations.
  Also for the PMA direct PAM4 a separate design is used instantiated with Reset Controller Bypass and the channel information is “dumped” in order to be used for the reconfiguration.

## Slide 21: Reset controller bypass
  Note that all resets need to be controlled manually when using RSFEC in fractured mode (and also for this specific case for the KPFEC in aggregate mode because of the DPRIO)
  See section 6.5.3 Reset Controller Bypass in the E-Tile Userguide.
  All these reset signals are being handled by the application software running on the Nios.

## Slide 22: Important note on reset control
  Since the reset is under software control, the reset will not be automatically triggered when e.g. the remote side will stop sending data. Even though the local link will come up automatically when this happens (without a specific reset) you will see errors being reported in some cases (and/or) PRBS Alarms will be asserted to illustrate something has happened.

## Slide 23: Regarding Independent Resets Supported in this design.
  When configured in RSFEC Fractured Mode
  Independent reset only possible on ch 1-3, resetting ch 0 (master channel) is also resetting the other channels (This is expected behavior)
  When configured in PMA direct mode 4x25G
  Independent reset is possible only on channels including master ch 0. So when a channel is being resetted the other channels will not be impacted.
  When configured in PMA PAM4 high datarate direct mode
  Only Phy level resets are possible in this mode.
  When configured in any Aggregate mode
  Only Phy level resets are possible in this mode (which is expected since it is aggregate).

## Slide 24: Channel Register Set
  The design is using 2 custom .qsys component that can be parameterized. The components are called “Channel Register Set” (using channel_reg_set_hw.tcl) and “Phy Register Set” (using phy_reg_set_hw.tcl) are available in the default group section of the Qsys library.
  These components can be parameterized to the number of phys and channels there are instantiated in the design and makes the generation of the Qsys system much more streamlined.
  As in this design 2 phy’s are being used the number of phy’s is set to 2 in the “Phy Register Set” and since each phy has 4 lanes the number of register set has been set to 8 in the “Channel Register Set”.

## Slide 25: Timing Closure (Setup)
The design is fully constraint without any timing violations
Compiled for 1ST280EY2F55E1VG

## Slide 26: Timing Closure (Hold)
The design is fully constraint without any timing violations
Compiled for 1ST280EY2F55E1VG

## Slide 27: Native Phy Debug Master Endpoint Interface
In addition to the AVMM interface the Native PHY also enable the Native Phy Debug Master Endpoint interface which can also be accessed through the Qsys system due to the addition of the jtag_debug_module.
Access to the Native Phy Debug Master Endpoint interface can be done through System Console totally in parallel while the Nios controller(s) are being used.
The Native Phy Debug Master Endpoint interface can be used for advanced debugging and reporting (see further) .
The major advantage of having the Native Phy Debug Master Endpoint interface is that it allows to run directly the Universal Toolkit (see further).

## Slide 28: Nios II Control & Monitoring
The Nios II controller is used to control and monitor the design using the Nios II terminal.
  Display status signals for each of the channels
    Encoding (PAM4/NRZ and gray and/or 1/1+D encoding)
    RSFEC Statistics
    Rx Termination setting
    LPM Setting
    Freq_Locked
    Pll_locked
    Rx_ready
    Serial Loop + Reverse Parallel Loop
    Channel Type
    Connection Type
    Rx Polarity Inversion
    Tx Polarity Inversion
    Adaptation Mode + PMA Configuration
    Status of the ADAPT_SIP (Searching/Success or Not active).
    Number of biterrors.
  Select which PRBS pattern should be used (PRBS-7, PRBS-9, PRBS15i,PRBS-23 or PRBS-31) on each channel if using the 64-bit PRBS generators and checkers. When PMA direct PAM4 is used one can use PRBS-13, PRBS-23 and PRBS-31.
  Displays the bitrate based on measured reference clock frequency and reference clock multiplication factor.
  Displays also the recovered clock frequency (of lane 0). Note that if lane 0 has no connection or is is not in serial loopback the measured recovered clock frequency is a random number as the CDR is not locked to anything.

## Slide 29: Nios II Control & Monitoring (continued)
  Option ‘4’ : dynamic reconfiguration option :
      Reconfigure all Phys to NRZ RSFEC Fractured (528,514) or reconfigurable r
      Reconfigure all Phys to NRZ RSFEC Fractured (544,514)
      Reconfigure all Phys to PAM4 RSFEC Fractured (544,514)
      Reconfigure all Phys to NRZ RSFEC Fractured (528,514) with only 2 even lanes active
      Reconfigure all Phys to PAM4 KPFEC Aggregate (544,514) with 2 physical lanes
      Reconfigure all Phys to NRZ PMA direct mode with 4 physical lanes
      Reconfigure all Phys to PAM4 PMA direct mode with 2 physical lanes.
      Reconfigure current selected channel to PMA direct mode with configurable rate (based on tx_clk_divider)
      Reconfigure current selected channel to RSFEC Fractured at nominal rate.
  NEW : Allows to reset an indepent channel to illustrate the reset independence (see Slide on Independent Reset for full details)
  Control Serial Loopback on all lanes and per phy.
  Control Reverse Parallel Loopback on all lanes and per phy.
  Control Swizzle on all lanes and per phy
  Control Invert Tx and Rx Polarity on all lanes and per phy
  Error insertion : Soft PRBS Biterror (Pre-FEC), PMA errors (0-99) (Post-FEC) or error insertion through RS-FEC directly.
  Control LPM Mode on a per channel basis (note LPM only works in mission mode).
  Displays the number of biterrors and the BER.
  Allows to reconfigure dynamically between NRZ and PAM4 mode.
  Allows to insert a biterror on the link.
  Displays the time the test has been running on the Transceiver Block.

## Slide 30: Nios II Control & Monitoring (continued)
  Measures the temperature of the core and the transceiver tile.
  Reads out and print out PMA settings for all channels
  Allows to find the optimum Transmit PMA settings (VOD, Pre-emphasis) using PMA sweep function. (Option ‘U’)
  Provides 3 different effort levels in terms of adaptation (zero, half or full) impacting the time it takes for the iADP to complete. Half effort level should be sufficient for most PAM4 connectivity, Zero effort level is the choice for NRZ.
  Allows to change the PMA configuration on the selected phy (10G,28G LR, 28G VSR, 56G LR, 56G VSR) (option ‘x’). This needs to be set before running the iADP on that PHY.
  (Option ‘z’) : This controls the ADAPT_SIP in each Native PHY : either the ADAPT_SIP can be started or stopped/reset.
  Dumps I2C information of connected modules and cables like Vendor, part number, cable length, temperature of the module.
  Allows to dump the I2C page Lower page and Page 00h registers of the selected module/cable
  Option ‘L’ : stress test submenu (see dedicated slide)

## Slide 31: Stress Tests
Option ‘L’ provides a submenu to perform the following “stress tests”:
Reset selected PHY 1000 times
Dynamic reconfiguration : toggle between Fractured and Aggregate mode 1000 times
Start/Stop Adaptation Soft IP 1000 times (serial loopback must be disabled)
Disable/Enable Phy1 Tx (tristate) in combination with Adapt SIP 1000 times
(note this requires physical connection between PHY1 and PHY0
(and PHY0 needs to have the Adapt SIP started
Toggle Disable/Enable Tx buffer and reset Tx 1000 times

## Slide 32: Important notes about how to use the software
The software performs a PMA reset of both phy’s when started, reset’s the soft ADAPT qsys systems, programs serial loopback and runs an initial adaptation.
Depending on the connection you have you can then disable the serial loopback (option ‘8’) on all the channels in a selected phy.
You can select a PMA configuration that matches your setup (option ‘x’) (optional).
To start the adaptation using the adaptation soft IP the easiest is to run option ‘z’ and select the option to start the search algorithm. Once it is started it will continously check for presence of valid signal and if signal is lost it will continuously start the algorithm again until it has been found..
One can then plug-out the module/cable (which will result in the algorithm searching again for a valid signal), this can be observed in a separate Nios terminal.
The flowchart of the search algorithm that is implemented in the Soft Adaptation IP is displayed on the following slide.
Note : To do all everything at once (i.e. disable serial loopback and start the adaptation SIP on both PHY’s use option ‘.’ )

## Slide 33: Search Algorithm Flowchart

## Slide 34: Starting the search algorithm on Soft IP Adapt 0 (With external QSFP-DD loopback (2.5 meter DAC)
The below is using a Nios terminal connected to the Adaptation Soft IP of PHY 0
(started using ./start0.bsh)

## Slide 35: Main Program status window after starting the Adaptation Soft IP on PHY 0 (5 meter cable) (this was measured with design without FEC with older software)
Using start2.bsh

## Slide 36: Starting the search algorithm on Soft IP Adapt 1 (With no cable connected)
The below is using a Nios terminal connected to the Adaptation Soft IP of PHY 1 (started using ./start1.bsh). As no physical connection is made, it will continue to run the algorithm until a valid signal becomes available

## Slide 37: Nios 2 Output in Nios II SDK Shell (start screen at speed of 25.78125 Gbps)

## Slide 38: PHY 0 connected to PHY1 with 2.5 Meter QSFP-DD cable at 25.78125 Gbps
PMA configuration : FW Default
Continuous adaptation
(Soft Adapt IP running)

## Slide 39: PHY 0 PMA settings

## Slide 40: Insert burst of RSFEC errors on PHY 0 on lane 2
Result shown is after inserting RSFEC errors on phy 0 lane 2 with (pat=0x01,rate=0x01)
All inserted RSFEC errors are being corrected by PHY1 as can be observed.

## Slide 41: PHY 0 connected to PHY1 with 2.5 Meter DAC cable at 53.125 Gpbs
Dynamically reconfigured to KPFEC Aggregate
Testresult after 1h 43 minutes.
PMA configuration : 56G LR
Continuous adaptation
Errorfree
Total number of corrected codewords : 18620.
SER : 2.82E-10.

## Slide 42: PHY 0 PMA settings

## Slide 43: PHY 1 connected to PHY0 with 2.5 Meter DAC cable at 53.125 Gpbs
Dynamically reconfigured to KPFEC Aggregate
Testresult after 1h 43 minutes.
PMA configuration : 56G LR
Continuous adaptation
Errorfree
Total number of corrected codewords : 30249
SER : 4.59E-10.

## Slide 44: PHY 1 PMA settings

## Slide 45: Reconfigure individual lane from RSFEC to PMA direct
Here lane 2 is reconfigured from RSFEC Fractured to PMA direct at 10.3125 Gbps. The reconfiguration is fully independent i.e. it is not impacting the other channels.

## Slide 46: Available commands

## Slide 47: Dynamic Reconfiguration Menu (option ‘4’)

## Slide 48: Readout of the I2C information
Every time a status update is done all QSFP-DD modules will be checked if anything is plugged in and if this is the case the I2C information will be readout.
See screenshot below showing various module and cables connected in the the system.
Information provided is Vendor, Part Number, temperature for modules and cable length for QSFP-DD cables or QSFP cables.
One can dump the entire I2C Lower Page and Page 00h using option ‘{‘

## Slide 49: Board setup (1/2)
Make connections to the QSFP-DD 2x1 (Using loopback modules, optical modules or cable).
Connect USB Cable to CN1 in order to use onboard USB-Blaster II.
Power on the board
Program the clocks using the Clock control GUI (see screenshot on next page, clocks highlighted in yellow
  Datarate is referenceclock frequency x 165 for NRZ RSFEC (528,514) Fractured so for 25.78125 Gpbs use 156.25 Mhz.
  Datarate is referenceclock frequency x 170 for PAM4 KPFEC Aggregate or RSFEC using (544,514) so for 53.125 Gpbs use also156.25 Mhz.
Note that each PHY runs from a different referenceclock input (with ppm differences between them)
Download ‘Devkit_Demo.sof’ to the 1ST280EY2F55E1VG device using QII 21.1 programmer

## Slide 50: Board setup (2/2)

## Slide 51: Running the software (1/2)
This is when you want to run the software available inside the program memory, Do the following :
  Start a Nios II command Shell (can be found in the Quartus installation (e.g. C:\quartus_21_1\nios2eds) and go to the directory where the start2.bsh file is located.
  Since 21.1 Nios II terminal is using WSL, a quick way to go to the selected directory is to copy the complete path using windows explorer and in the Nios 21.1 terminal you type cd "$(wslpath “ => then you paste the path you copied (using right mouse click) => and end with typing ")“
    e.g. cd "$(wslpath " C:\ALTERA\Reference_Designs\PRBSTEST\Stratix10TX\prbs_2x4ch_ETILE_26Gbps_qsfp_2x1_ODI_softIP_RSFEC_Frac\software\app\Stratix10GX_xCh ")“
  Since the quartus archive is restored in windows the files need to be converted from Dos to Linux. To do so either use “dos2unix –k *” or run the provided .bsh file “./convert.bsh” (note option –k keeps the original date of the file intact).

## Slide 52: Running the software (2/2)
  Type In The Following Command : “./start2.bsh” This will set the JtagSpeed to 16M and start the Nios II code embedded inside the main program memory.
  (optional) : To connect to the Soft ADAPT IP of PHY 0 open an additional Nios II 21.1 terminal and repeat the steps on the previous slide to go to the right directory. Type In The Following Command : “./start0.bsh” .
  (optional) : To connect to the Soft ADAPT IP of PHY 1 open an additional Nios II 21.1 terminal and repeat the steps on the previous slide to go to the right directory. Type In The Following Command : “./start1.bsh” .

## Slide 53: Running the software (Alternative)
  Start a Nios II command Shell (can be found in the Quartus installation (e.g. C:\quartus_21_1\nios2eds) and go to the directory where the .run2.bsh and .elf file are located.
  Since 21.1 Nios II terminal is using WSL, a quick way to go to the selected directory is to copy the complete path using windows explorer and in the Nios 21.1 terminal you type cd "$(wslpath “ => then you paste the path you copied (using right mouse click) => and end with typing ")“
    e.g. cd "$(wslpath "C:\ALTERA\Reference_Designs\PRBSTEST\Stratix10TX\prbs_2x4ch_ETILE_26Gbps_qsfp_2x1_ODI_softIP_RSFEC_Frac\software\app\Stratix10GX_xCh")“
  Since the quartus archive is restored in windows the files need to be converted from Dos to Linux. To do so either use “dos2unix –k *” or run the provided .bsh file “./convert.bsh” (note option –k keeps the original date of the file intact).
  Type In The Following Command : “./run2.bsh” This will set the JtagSpeed to 16M download the .elf file and start the Nios II code embedded inside the main program memory.

## Slide 54: Rebuilding the software
In order to rebuild the software do the following (using QII 21.1 or later):
Start a Nios II 21.1 Command Shell
  go to the ../software/app/Stratix10GX_xCh directory (which is part of the archive) using the method descriped on the previous slide
  Run the bash file ./convert.bsh (this will also convert the files in the bsp folder)
  Run ./create-this-app .This will compile the system libraries (in the bsp folder), compile the software code (main.c and a number of other .c files in this case) and produce a Nios II executable.
If you make any changes to the software you need to rebuild by typing “make” in the Nios II 20.4 shell (after having created the software a first time)
To run the software : type In The Following Command : “./run2.bsh” This will set the JtagSpeed to 16M and download the Nios II code to the FPGA and open up the terminal.

## Slide 55: Use of Native Phy Debug Master Endpoint (Optional)
To access the Native Phy Debug Master Endpoint, open the System Console.
Please download or start first the Nios design as otherwise access to system console might be compromised.
From here you have access to all AVMM registers from the transceivers.

## Slide 56: UTK_helper_s10tx.tcl Script
In the folder “scripts” one can find a useful UTK_helper_s10tx.tcl file that has a library of procedures similar to the ones used in software, ranging in complexity from reading a register to performing adaptation on all channels at the same time.
Most of the procedure require to identify the “phy” on which the action to perform. To identify the “phy” one can just use a unique string that identifies the native phy as it exists in the RTL code.
When sourcing the UTK_helper_s10tx.tcl script you will get the identification automatically and the slave address helps identifying the PHY in the UTK.
Below is the list of E-tile PHY's claimed
Use etile_phy_<i> as phy identifier in the functions
Phy : "etile_phy_41" ---> Hierarchy Path: {Generate_transceiver_block[0].instx|generate_adapt_sip.xcvr_txrx_inst|xcvr_native_s10_etile_0|alt_xcvr_native_optional_rcfg_logic} Slave: 0x1800000
Phy : "etile_phy_43" ---> Hierarchy Path: {Generate_transceiver_block[1].instx|generate_adapt_sip.xcvr_txrx_inst|xcvr_native_s10_etile_0|alt_xcvr_native_optional_rcfg_logic} Slave: 0x2000000

## Slide 57: UTK_helper_s10tx Script (continued)
So to identify PHY0 one can simply use etile_phy_41 e.g. to address that specific phy.
The list on the following slides shows the available procedures and provides examples how to use them.

## Slide 58: UTK_helper_s10tx Script (Generic functions)
rmw_all {offset mask newval verbose}
example useage rmw_all 0x160 0x0E 0x03 1
rmw_channel {phy channel offset mask newval verbose}
example useage rmw_channel etile_phy_42 0 3 0x40000 0x0F 0x03 1
rd_channel {phy channel offset verbose}
to read and printout use e.g. rd_channel etile_phy_42 3 0x40000 1
when only reading without printing use e.g. set d [rd_channel etile_phy_42 3 0x40000 0]
rd_all {offset}
example useage rd_all 0x40011
raw_dump_channel {phy ch start_addr stop_addr}
example useage raw_dump_channel etile_phy_42 0 0x000 0x300
compare_xcvr_channels {phy ch1 ch2 start_addr stop_addr}
example useage compare_xcvr_channels etile_phy_42 0 1 0x0 0xF

## Slide 59: UTK_helper_s10tx Script (E-Tile specific part 1)
rcfg_etile {phy channel interrupt_code interrupt_data verbose}
example useage reading vod : set readback_vod [rcfg_etile etile_phy_42 0 0x15 0x4100 1]
example useage writing vod setting 3 : set readback_vod [rcfg_etile etile_phy_41 0 0x15 0x4003 0]
start_check_prbs_etile {phy channel pattern verbose}
example to start prbs31 on channel 1 of etile_phy_42 : start_check_prbs_etile etile_phy_42 1 31 1
set_loopback_etile {phy channel serial_loop rev_parallel verbose}
example to set serial loopback on channel 4 of etile_phy_42 : set_serial_loopback_etile etile_phy_42 4 1 0 1
set_mode_etile {phy channel rx_termination line_encoding tx_clk_divider rx_clk_divider gray_encoding encoding_1_1plusd verbose}
example to set PAM4 on channel 4 of etile_phy_42 with gray_encoding and rx_termination set to VCC : set_mode_etile etile_phy_42 4 1 PAM4 0x64 0x64 1 0 1
reset_uc {phy channel verbose}
example to reset uc on channel 2 of etile_phy_42 : reset_uc etile_phy_42 1 1
reset_uc_phy_etile {phy verbose}
example to reset uC on all channels of etile_phy_42 : reset_uc_phy_etile etile_phy_42 1

## Slide 60: UTK_helper_s10tx Script (E-Tile specific part 2)
iadp_channel {phy channel verbose}
example to run iadp on channel 1 of etile_phy_41 iadp_channel etile_phy_41 1 1
iadp_phy {phy verbose}
example to run iadp at once on all channels of etile_phy_41 : iadp_phy etile_phy_41 1
set_serial_loopback_phy_etile {phy serial_loop verbose}
example to turn serial loopback ON for all channels of etile_phy_41 : set_serial_loopback_phy_etile etile_phy_41 1 1
start_check_prbs_etile {phy channel pattern verbose}
example to start prbs31 on channel 1 of etile_phy_33 : start_check_prbs_etile etile_phy_33 1 31 1
start_check_prbs_etile_all {pattern verbose}
example useage to start prbs31 on all channels start_check_prbs_etile_all 31 1

## Slide 61: UTK_helper_s10tx Script (E-Tile specific part 3)
check_prbserror_etile_all {verbose}
example useage to continously check errorcount on all tiles check_prbserror_etile_all 1
inject_error_etile {phy channel number_of_errors verbose}
example to insert 3 biterrors on channel 1 of etile_phy_33 : inject_error_etile etile_phy_33 1 3 1
reset_errorcount_etile {phy channel verbose}
example to reset prbs errorcount on channel 1 of etile_phy_33 : reset_errorcount_etile etile_phy_33 1 1
get_prbs_errorcount_etile {phy channel verbose}
example to get prbscount on channel 1 of etile_phy_33 : get_prbs_errorcount_etile etile_phy_33 1 1
run_test_all {pattern serial_loop adaptation_mode verbose}
example useage to start prbs31 on all channels with serial loopback and 0.5 iADP : run_test_all 31 1 0.5 1

## Slide 62: UTK_helper_s10tx Script (E-Tile specific part 4)
get_firmware {phy}
example to get firmware version : get_firmware etile_phy_41
powerdown_serdes {phy verbose}
example to powerdown all channels of etile_phy_43 : powerdown_serdes etile_phy_43 1
powerup_serdes {phy verbose}
example to powerup all channels of etile_phy_43 : powerup_serdes etile_phy_43 1

## Slide 63: Using Universal Toolkit (Optional)
To start the Universal Toolkit simply start it from the Tools Menu in Quartus (with the project loaded). This will automatically detect the design and start up the Universal Toolkit which allows you to run further tests in optimizing the PMA settings, do autosweeps etc.
Make sure to stop all traffic running in UTK and close the UTK before going back to the Nios terminal to continue with the design (If the hard PRBS generator and checker have been enabled during testing those channels will show errors (which is normal). Using option ‘q’ these errors can be cleared

## Slide 64: Eye Scan using Universal Toolkit
The screenshot below shows the Eye measurement on channel 0 running at 25.7815 Gbps with 2.5 meter QSFP-DD cable.
To avoid conflicts during measurement, make sure the adapt_sip is not running a the time the measurement is taken.

## Slide 65: Signaltap II Debug Example
The design contains a number of signaltap instances
Signaltap II acquisition can be done simultaneously with Nios II control.

## Slide 66: TestBench
First steps :
Open a Nios II 21.1 Command Shell and go to the simulation directory (see section “Running the software” on how to change the directory in an easy way)
Run dos2unix –k *
Run ./create_simscript.bsh (for Windows)
On linux use ./create_simscript_arc.bsh (for ARC/Linux environments) instead.
This will create the necessary simulation scripts to match your own environment.
When using Modelsim SE (or PE) or Questasim (tested with QuestaSim 10.5c)
  Go to the folder ../simulation/mentor
  Run ‘Sim.do’ do compile and simulate everything (when there are no libraries yet)
  Run ‘Resim.do’ when libraries already exist to re-compile only the design files and simulate the testbench
The simulation files can be found in the ‘simulation/mentor’ directory
The testbench will also insert 2 errors which are reported by the testbench.
The testbench also controls the reset signals required for the manual reset control required for the RSFEC operation.

## Slide 67: Deliverables
Quartus 21.1 B169 archive which contains the demo design files, the software source files, ttk_helper_s10tx.tcl scripts and the testbench files.
The testbenches can be found after restoring the archive: <restored_project>/simulation
The software source files can be found after restoring the archive in the <restored_project>/software/app and <restored_project>/software/bsp folders/
The software source file for the soft IP Adaptation algorithm can be found after restoring the archive in the <restored_project>/core_prbs/software_adapt_sip/app and <restored_project>/core_prbs/software_adapt_sip/bsp folders.
SOF File (including the Nios program for the main program as well as the Nios programs for the soft ADAPT IP)
ttk_helper_s10tx.tcl file in the /scripts folder
Readme.txt file

## Slide 68: Status & Revision
V21.1 : June 7th 2021
  Changed the dynamic reconfiguration options to allow reconfigurable rates on all configurations.
  Fixed bug that showed issue with PAM4 high datarate coming properly out of reset
V21.1 : June 1st 2021
  Major update to the design to allow to dynamically reconfigure a channel independently from Rsfec fractured to PMA direct mode and individually reset support
    Added 8 clock multiplexers per PHY instance
    Added phase comp FIFO’s for the clock domain crossings because of the clock multiplexers
    Updates to the software to allow for independent channel reconfiguration.
  Uses Mailbox Client IP and Nios HAL to readout the temperatures instead of temperature sense IP.

## Slide 69: Status & Revision
V20.4 : January 7th 2021
  Updated all IP to 20.4
  Added PrbsAlarm signal : the PrbsAlarm signal will be asserted when the PrbsLock will go down (due to external causes e.g. cable pull/plug in) and remain asserted until a reset errorcount or reset of the phy is being done. This allows to capture any events that could occur that could bring down a link for a period of time to keep track of this.
V20.3 : December 7th 2020
  Updated IP to 20.3
  Updated PRBS generators and verifiers.
  Updated Adapt_SIP software.
  Added BTI Mitigation (Preserve Unused Channels)
V20.2 : August 13th 2020
  Use different “seeds” for 64-bit prbs generators.
  Updated design to also allow to reconfigure to PAM4 PMA direct which is using a different datapath and 128 bit PRBS generators and checkers.

## Slide 70: Status & Revision
V20.1 : June 17th 2020
  Updated Adapt SIP search algorithm according to the latest guidelines.
  Added optional scrambler/descrambler option
  Added additional RSFEC statistics.
  Added PMA error injection (post-FEC)
  Added stress tests in software (reset tests, adapt sip tests etc.)
V20.1 : May 26th 2020
  Added dynamic reconfiguration to PMA direct mode
  Consolidated the dynamic reconfiguration options into one menu option and reconfigure always both phys in all cases.
V20.1 : May 13th 2020
  Transitioned to 20.1
  Added functionality : when in 4 lanes fractured allows to reconfigure the RSFEC from (528,514) to (544,514) for NRZ and allows to reconfigure to PAM4 on all 4 lanes using RSFEC (544,514).
  GUI updates (with color coding)

## Slide 71: Status & Revision
V19.3 : March 11th 2020
  Added functionality to support 2 lanes of NRZ RSFEC Fractured (using the same physical lanes as the PAM4 configuration). The PMA of the odd channels (not used) is disabled to save power.
  Changed relevant software makefiles to support Nios II 19.3 Command Shell (using WSL) (no need to have Nios II 19.1 Command shell any longer).
V19.3 : March 5th 2020
  Initial version
  Succesfully tested 1000 reconfigurations between RSFEC Fractured and KPFEC aggregate.

## Slide 72: Feedback and/or Questions?
Peter Schepers (peter.schepers@intel.com )
+32 495 57 32 22