## Slide 1: Stratix10 TX ‘Superlite IV’ Demo Design V18.1.1 for the Stratix10 TX SI Board 4 Lanes @ 53.125 Gbps routed to the QSFP-DD modules Using NATIVE PHY + KPFEC (No EHIP)
Peter Schepers
Technology Specialist FAE High Speed Interfaces
February 12th, 2019

## Slide 2: Introduction & Motivation
This design illustrates how to use the Superlite IV concept on Stratix10 Tx using the E-Tile
This version is only using Native PHY with PAM4 with RSFEC configured in RS(544,514)(aka “KPFEC” aggregrate mode. No EHIP Core or EHIP Lane is being used.
  This version is using PAM4 at 53.125 Gbps
  Link information is exchanged between the local and remote side and results in a LinkUp when both local and remote side are aligned.
  XOFF is used in order to allow for backpressure or Flow Control: ask remote side to stop sending traffic (when local side e.g. is not capable of receiving the data).
  This demo design is using 2 instances of the Superlite IV demo instance, each with 2 lanes running at 53.125 Gbps PAM4 and each connected to the QSFP-DD module. Using DAC or Fiber Optic connection a full system test can be done between the 2 modules, illustrating link-up, reset behaviour etc.

## Slide 3: ‘Superlite IV’ Concept

## Slide 4: ‘SuperLite IV’ Concept
Transport data from point A to point B as simple as possible multiple bidirectional serial links.
This version of Superlite IV only makes use of the Native PHY which can be used with NRZ or PAM4 and with and without FEC (for NRZ only). This allows to use all available lanes inside the E-tile (as opposed to the EHIP version which can only use the lanes next to the EHIP CORE for the PAM4).
This particular demo is using PAM4 and KPFEC. Future demo’s will use NRZ with FEC as well (Version without FEC already exists (Superlite II V4).
Like in Superlite II, Superlite IV also exchanges information between local and return side (handshaking) as well as allows to sent XON/XOFF control (backpressure)
On the transmit side data will only be written in the FIFO when the valid signal is asserted, the fifo also can issue a backpressure signal (indicated by the ‘ready’ signal to indicate if data can be transmitted. This is equivalent to the Avalon Streaming interface.
When XOFF is received from the remote side, all traffic will be halted on the local side (link remains running though).
All the logic is clocked on one single clock (i.e. both transmit and receive core logic), this clock is the clock derived from the transmit PLL and is basically the line rate/128 for the PAM4 high datarate case.
This implies that the combination of data valid with the locally generated clock from the local transmit PLL is frequency locked to the clock used at the remote side (which will typically vary in ppm). PPM difference is also measured inside the design.
As the Native PHY mode with PAM4 and KPFEC is only available as a “block” with 2 lanes, the amount of lanes is always a multiple of 2 for the high datarate PAM4 version.
Multiple HIP’s can be used in combination in order to have a multiple of 2 lanes (see the 1x8 lanes demo design and 1x12 demo designs).

## Slide 5: ‘Superlite IV’ Concept (continued)
For aligning the lanes across multiple Native PHY idle characters and alignment characters will be sent at regular intervals (at the same pace as the generation of the mandatory Alignment marker insertion). Alignment markers need to be inserted every 80K parallel clock cycles.
The Superlite IV TX module will automatically pause Tx user data if needed to insert idle and alignment characters and will also pause Tx user data based on the “ready” received from the EHIP (as it is working in overspeed). So the userdata needs to be able to immediately stop sending traffic. If this is not possible one can add an additional FIFO with a slower running write clock
User data is always in multiple of 256 bits as this is the granularity of the Native PHY with KPFEC in PAM4 high datarate mode.
The amount of physical lanes used in this demo is 2 lanes per Superlite IV instance. This corresponds to 4 virtual lanes per Superlite IV instance (which is what the KPFEC will inherently use).

## Slide 6: ‘SuperLite IV 4 (2x2) lane Demo Design
Goals :
  Demonstrate the Superlite IV concept on Stratix10 TX using only Native PHY
    Use Stratix10 TX Signal Integrity board as platform for demonstration.
      Uses 2 Superlite IV demo instances (each with their own packet generator and checker). Each instance (or “phy”) is connected to the QSFP-DD module
      Full system validation can be done using a DAC cable (various length) between the 2 QSFP-DD modules.
    Line rate in this demo is 53.125 Gbps per lane but using a higher referenceclock frequency it can be overclocked to run at e.g 57.8 Gbps per lane..
    2 Different reference clocks will be used, to show it can work with ppm differences
    2 lanes will be used for each phy, therefore aggregate line rate is 106.25 Gbps per phy
    User data width is 256-bits (64 bits per virtual lane) per phy
    Actual throughput is measured in the design by measuring the data_valid received in combination with the clock. The net datarate is 99.985 Gbps (so slightly less than 100 Gbps, because of KP FEC overhead, AM overhead and idle/alignment insertion).
    The user data is generated based on the 415.039 Mhz clock generated by the Native PHY (line rate divided by 128). As it receives backpressures from the Superlite IV Tx module the data will be halted at specific times.

## Slide 7: Goals (continued)
Goals :
  To create the 256 bit user data to each phy a combination of different counterpatterns and prbspatterns are used across the 4 virtual lanes of each instance.
  Uses Reconfiguration Management Interfaces for the E-tile transceiver and reconfiguration interface of the RSFEC through a QSYS system.
  Through ADME Transceiver Toolkit support is automatically available.
  Use Nios II processor as controller/monitor.
  The RAM in the QSYS is programmed with the latest software, so one can directly connect to the system using JTAG and run the software.
  Reports and calculates all relevant RSFEC statistics to provide information on the RSFEC performance.
  Reports errorcount and calculates BER based on the received data.
  Includes Testbench

## Slide 8: ‘Superlite IV’ Resources (one phy)
Superlite IV Etile TxRx Module Resources 2 lanes at 53.125 Gbps.
Note : Note that this version is not using any Receive FIFO’s as the data is already aligned by the the RSFEC.
  ~ 2350 ALUT’s
  ~ 1950 ALM’s
  ~ 2750 Dedicated logic registers
  7 M20K (for the transmit buffer)

## Slide 10: Tx Path
A datastream is generated at a clock of 415.039 Mhz @ 256 bit when DataIn_ready is high. The datapattern is a combination of 4 60-bit Prbs-23 (each with their own starting value) and one 16-bit counterpattern.
  The 16-bit counterpattern is spread across the 4 lanes, 4 bits per lane. This is to make sure any deskew on the lanes would be immediately spotted.
Since idle +alignment characters and AM markers have to be inserted at regular intervals and because of the overclocking the IP is generating periodic tx_pcs_ready pulses. So the data stream will be halted at regular intervals. This is indicated by the Superlite IV TX module by the DataIn_ready signal.
Single biterrors can be inserted using inserterror input. As there is one PRBS-generator per virtual lane, the biterror insert will produce 4 bit-errors at a time.
This data is presented to the Superlite IV Tx Module
The data is written into the TxFifo (single clocked fifo) using the 415.039 Mhz as clock and using the DataIn_Valid as write-enable.
The read_enable of the TxFifo is pulsed at the same pace as the write-enable.
Once every 80K valid cycles idle characters + alignment characters + alignment markers will be inserted in the datastream. If no valid data is present idle characters will be sent.

## Slide 11: Tx Path (continued)
The scrambling is being done in the txrx_pcs_64b66_kpfec module. The scrambler is working in 100GbE mode (mandatory for the KPFEC).
The special control characters being used for idle and alignement are the following :
In terms of idle character a value of “00….00BCFF” is being used (valid 802.3 control character). The alignment character is sent as the last control character. The lower 16 bits of this control word (at the alignment position) encodes the status of the link in addition to the alignment indication.
If no local alignment has been found : the last control word sent is “..7CFF”
If local wordalignment has been found : the last control word sent is “..FDFF”
If XOFF is being sent to the remote side : the last control word sent is “..5CFF”
If local side is not transmitting : the last control word sent is “..3CFF”
If local side is not transmitting and XOFF is being sent to the remote side : last control word sent is “…9CFF”.

## Slide 12: Rx Path
Each Native PHY + KPFEC will perform all necessary wordalignment, decoding, deskew of the virtual lanes, RSFEC dedoding + correction and will present 256 bits of aligned data and control to the user (in combination with a valid signal and received alignment markers (which can be discarded). External soft IP is used to deskew the received data to make sure the received data is properly deskewed across the AIB.
To deskew the data received from multiple HIP instances (if applicable) the following method will be used : Based on the position of the alignment word, the delay for each block is measured and the statemachine inside the Rx_path_deskew module will use the information of that measured delay to control the readenable to the RxFIFO’s to deskew all the virtual lanes. Note in this demo design there is only one block so the RxFIFO’s are not instantiated.
Once lane alignment is achieved amongst all instances, the combined data in addition with a data valid signal will be sent to the data verifier.
Here PRBS and counterverification will take place and single biterrors will be counted.
Prbslocked is asserted when 128 consecutive valid Prbs-23 60-bit words have been received on each of the virtual lanes and de-asserted when 128 consecutive non-valid Prbs-23 60-bit words have been received.
Countlocked is asserted when 128 consecutive valid 16-bit counter words have been received on the parts of the virtual lanes they were received.
There are 4 60 bit PRBS Verifiers (one for every virtual lane) and 1 16-bit CountVerifier to validate the 256 bit data.

## Slide 13: Rx Path (continued)
The V3 version adds an additional Rx State machine to the logic to determine the local Rx state and it depends on the incoming “alignment” control word
If last control word received is “…FD7C” it means the remote side has reached Wordalignment, if local side also has reached wordalignment this results in Linkup to be asserted, indicating that both sides are up and running. This can be used as the trigger to sent data across e.g.
If last control word received is “…5C7C” it means an XOFF has been received from the remote side, this will be forwarded to the local transmitter to stop generating traffic on the local side.
If last control word received is “…3C7C” it means the remote side has stopped sending traffic (as a response to a local XOFF)
If last control word received is “…9C7C” it means the remote side has stopped sending traffic but at the same time also requesting XOFF. At this point of time both local and remote side are not generating any traffic (Link is still up).

## Slide 14: E-Tile Native PHY (TX PMA/RX PMA)

## Slide 15: E-Tile Native PHY (RSFEC)

## Slide 16: E-Tile Native PHY (Core Interface)
Note : External clock mode is mandatory and tx_coreclkin2 will be fed by tx_clkout2 clock running at 2x the datarate

## Slide 17: E-Tile Native PHY (PMA Interface)

## Slide 18: E-Tile Native PHY (Reset/Dynamic Reconfiguration)

## Slide 19: Link Register Set
  The design is using a custom .qsys component that can be parameterized. The component is called “Link Register Set” (using link_reg_set_hw.tcl) and is available in the default group section of the Qsys library.
  This component can be parameterized to the number of PHY’s or instances you want to instantiate in your design and makes the generation of the Qsys system much more streamlined.
  As in this design 2 phy’s are being used, the number of link register sets has been set to 2 in this design.
  For every Link that you use in your design it will generate a number of registers (to control/readout the measured clocks) as well as all the required AVMM reconfiguration interfaces for the E-Tile Hard IP (which is for every instance : 1 AVMM for the transceivers (shared interface) and 1 AVMM for the RSFEC).
  For the AVMM interfaces the Link Register set is calling another custom component : “reconfig_mgmt” (reconfig_mgmt_hw.tcl)

## Slide 20: Timing Closure
The design is fully constraint and has no timing violations.
Compiled for 1ST280EY2F55E2VGS1

## Slide 21: ADME Interface
In addition to the AVMM interfaces the ADME interface (Altera Debug Master Endpoint) is also enabled by default in the Ethernet HIP
Access to the ADME interface can be done through System Console totally in parallel while the Nios controller is also being used.
The ADME interface can be used for advanced debugging and reporting (see further) .
One advantage of having the ADME interface is that it allows to run directly the Transceiver Toolkit (see further).

## Slide 22: Nios II Control & Monitoring
The Nios II controller is used to control and monitor the design using the Nios II terminal.
  Display status signals (for each “Phy”)
    Freq_Locked
    Pll_locked
    RSFEC Status (tx_lanes_stable, cdr_lock, rx_am_lock …)
    RSFEC statistics
    Link Up
    DataLocked (combination of the 4 PrbsLocked and Countlocked)
    LaneAligned
    Effective Datarate
    Latency (only when looped back on it’s own)
  Control Serial Loopback on all lanes.
  Generate single biterrors in the generated data (note that inserting an error will result in 4 errors being seen : one per lane.
  Displays the number of biterrors and the BER.

## Slide 23: Nios II Control & Monitoring
  Allows to start a continuous BER measurement with a controllable interval (default time interval is 2 seconds).
  Displays the time the test has been running.
  Displays the measured reference clock frequency (Measured with 100 Mhz reference clock during 1 second).
  Measures the minimum and maximum latency (only when looped back to itself)
Access is through Nios SDK shell (see further)

## Slide 24: Nios 2 Output in Nios II SDK Shell (start screen at default speed of 53.125 Gpbs)

## Slide 25: Status PHY 0 (5 meter DAC)
During the test of 1 hour 11 minutes the entire link has been errorfree due to the KPFEC which performed correction of more than 5 million codewords during this timeframe.
As can be seen various important RSFEC statistics are provided, like pre corrected BER and Symbol error ratio.

## Slide 26: Status PHY 1 (5 meter DAC)
The same for PHY 1 : no biterrors observed.

## Slide 27: Losses associated with 5 Meter DAC cable
Cable used : 5m (16.4') 100GbE QSFP28 Cable - Amphenol 100-Gigabit Ethernet Passive Copper QSFP Cable (SFF-8665 802.3bj) - QSFP28 to QSFP28 (26 AWG)
https://www.cablesondemand.com/category/QSFP%20100G/product/SF-NDAAFJ100G-005M/URvars/Items/Library/InfoManage/.htm
See following slides for measured Insertion loss for both the board and the cable.
Cable insertion loss is ~ 20 dB at 13.28 Ghz.
Board insertion loss (TX+RX) is estimated to be at ~ 8 dB at 13.28 Ghz.
Connector insertion loss (estimate : 0.5 dB)
So total insertion loss at 13.28 Ghz (53.125 Gbps PAM4) ~29 dB.

## Slide 28: Cable Insertion Loss 5 meter DAC Cable

## Slide 29: Overclocking the design to run at 57.8 Gbps
By changing the 2 referenceclocks to use 170 Mhz instead of 156.25 Mhz the design can be overclocked to run at 57.8 Gbps (maximum PAM4 speed) and the design is still fully functional and errorfree

## Slide 30: Status PHY 0 (5 meter DAC) At 57.8 Gbps
During the test of 6 minutes no errors have been detected. Of course the SER is now significantly higher so the # corrected codewords is also higher at this higher speed.

## Slide 31: Status PHY 1 (5 meter DAC) At 57.8 Gbps
Similar for PHY1, no errors observed.

## Slide 32: Available commands

## Slide 33: Measuring Latency
Option ‘M’ is measuring the maximum latency across 1000 resets and provides a histogram of this maximum latency being measured. (this can only be measured when qsfp_to_qsfp is set to 0 in the main.c and an external loopback is used or when all lanes are in serial loopback (this is automatically checked)).
As can be seen maximum latency is on average 116 parallel clock cycles which is ~ 279 ns at 53.125 Gbps.

## Slide 34: Board setup (1/2)
Connect DAC cable between the 1x2 QSFP-DD Module (U32) and (U75).
Connect USB Cable to CN1 in order to use onboard USB-Blaster II.
Power on the board
Program the clocks using the Clock control GUI (see screenshot on next page, clocks highlighted in yellow
Download ‘Devkit_Demo.sof’ to the 1ST280EY2F55E2VGS1 device using QII 18.1.1 programmer

## Slide 35: Board setup (2/2)

## Slide 36: Running the software (Option 1)
The programming file already contains the program running on the Nios. To connect to the design do the following
Open a command prompt and run “nios2-terminal -c 1”
(if not already in the $path variable the nios2-terminal.exe can be found in the Quartus installation e.g. C:\quartus_18_1\quartus\bin64)

## Slide 37: Running the software (Option 2)
This is when you want to run a newer version of software (i.e. more recent to the version contained in the .sof file)
Do the following :
  Start a Nios II command Shell (can be found in the Quartus installation (e.g. C:\quartus_18_1\nios2eds) and go to the directory where the .elf file and run.bsh file is located.
  Type In The Following Command : “./run1.bsh” This will set the JtagSpeed to 16M and download the Nios II code to the FPGA and open up the terminal.

## Slide 38: Rebuilding the software (optional)
In order to rebuild the software do the following (using QII 18.1.1 B263 or later):
Start a Nios II 18.1 Command Shell and go to the ../software/app/Stratix10GX_xCh directory (which is part of the archive) and type: ./create-this-app .This will compile the system libraries (in the bsp folder), compile the software code (main.c and a number of other .c files in this case) and produce a Nios II executable.
If you make any changes to the software you need to rebuild by typing “make” in the Nios II 18.1 shell (after having created the software a first time)

## Slide 39: Use of ADME (Optional)
To access the ADME, open the System Console.
Please download or start first the Nios design as otherwise access to system console might be compromised.
From here you have access to all AVMM registers from the transceivers.

## Slide 40: Ttk_helper_s10tx.tcl Script
In the folder “scripts” one can find a useful ttk_helper_s10tx.tcl file that has a library of procedures similar to the ones used in software, ranging in complexity from reading a register to performing adaptation on all channels at the same time.
Most of the procedure require to identify the “phy” on which the action to perform. To identify the “phy” one can just use a unique string that identifies the native phy as it exists in the RTL code.
When sourcing the ttk_helper_s10tx.tcl script you will get the identification automatically and the slave address helps identifying the PHY in the TTK.
Below is the list of E-tile PHY's claimed
Use etile_phy_<i> as phy identifier in the functions
Phy : "etile_phy_18" ---> Hierarchy Path: {\Generate_Superlite_IV_Instances:0:instx|superliteiv_txrx_module_inst|txrx_pcs_64b66b_inst|xcvr_txrx_inst|xcvr_native_s10_etile_0|alt_xcvr_native_optional_rcfg_logic} Slave: 0x1800000
Phy : "etile_phy_20" ---> Hierarchy Path: {\Generate_Superlite_IV_Instances:1:instx|superliteiv_txrx_module_inst|txrx_pcs_64b66b_inst|xcvr_txrx_inst|xcvr_native_s10_etile_0|alt_xcvr_native_optional_rcfg_logic} Slave: 0x2000000

## Slide 41: Ttk_helper_s10tx Script (continued)
So to identify PHY1 one can simply use etile_phy_20 e.g. to address that specific phy.
The list on the following slides shows the available procedures and provides examples how to use them.

## Slide 42: ttk_helper_s10tx.tcl Script (Generic functions)
rmw_all {offset mask newval verbose}
example useage rmw_all 0x160 0x0E 0x03 1
rmw_channel {phy channel offset mask newval verbose}
example useage rmw_channel transceiver_block:0 0 3 0x40000 0x0F 0x03 1
rd_channel {phy channel offset verbose}
to read and printout use e.g. rd_channel etile_phy_36 3 0x40000 1
when only reading without printing use e.g. set d [rd_channel etile_phy_36 3 0x40000 0]
rd_all {offset}
example useage rd_all 0x40011
raw_dump_channel {phy ch start_addr stop_addr}
example useage raw_dump_channel etile_phy_36 0 0x000 0x300
compare_xcvr_channels {phy ch1 ch2 start_addr stop_addr}
example useage compare_xcvr_channels etile_phy_36 0 1 0x0 0xF

## Slide 43: Ttk_helper_s10tx Script (E-Tile specific part 1)
rcfg_etile {phy channel interrupt_code interrupt_data verbose}
example useage reading vod : set readback_vod [rcfg_etile etile_phy_36 0 0x15 0x4100 1]
example useage writing vod setting 3 : set readback_vod [rcfg_etile etile_phy_36 0 0x15 0x4003 0]
start_check_prbs_etile {phy channel pattern verbose}
example to start prbs31 on channel 1 of etile_phy_37 : start_check_prbs_etile etile_phy_37 1 31 1
set_serial_loopback_etile {phy channel serial_loop verbose}
example to set serial loopback on channel 4 of etile_phy_36 : set_serial_loopback_etile etile_phy_36 4 1 1
set_mode_etile {phy channel line_encoding tx_clk_divider rx_clk_divider gray_encoding encoding_1_1plusd verbose}
example to set PAM4 on channel 4 of etile_phy_36 with gray_encoding : set_mode_etile etile_phy_36 4 PAM4 0x64 0x64 1 0 1

## Slide 44: Ttk_helper_s10tx Script (E-Tile specific part 2)
iadp_channel {phy channel verbose}
example to run iadp on channel 1 of etile_phy_36 iadp_channel etile_phy_36 1 1
iadp_phy {phy verbose}
example to run iadp at once on all channels of etile_phy_36 : iadp_phy etile_phy_36 1
set_serial_loopback_phy_etile {phy serial_loop verbose}
example to turn serial loopback ON for all channels of etile_phy_36 : set_serial_loopback_phy_etile etile_phy_36 1 1
precal {phy prbspattern line_encoding tx_clk_divider rx_clk_divider gray_encoding encoding_1_1plusd verbose}
example to run precal with prbs31 with pam4 on on all channels of etile_phy_37 : precal etile_phy_37 31 PAM4 0x64 0x64 1 0 1
precal_simple {phy prbspattern exit_mode verbose}
example to run precal with prbs31 on all channels of etile_phy_37 and turn off prbs31 after calibration : precal_simple etile_phy_37 31 OFF 1
get_firmware {phy}
example to get firmware version : get_firmware etile_phy_36

## Slide 45: Using Transceiver Toolkit (Optional)
To start the Transceiver Toolkit simply start it from the Tools Menu in Quartus (with the project loaded). Using 18.1 or later.
This will automatically detect the design and start up the Transceiver Toolkit which allows you to run further tests in optimizing the PMA settings, do autosweeps etc.
Make sure to stop all traffic running in TTK and close the TTK before going back to the Nios terminal to continue with the design.

## Slide 46: Signaltap II Debug Example
The design contains a number of signaltap instances
Signaltap II acquisition can be done simultaneously with Nios II control.

## Slide 47: TestBench
First use : Open a Nios II 18.1 Shell and go to the simulation directory. In the shell provide the following command “./create_simscript.bsh”. This will create the necessary simulation scripts to match your own environment.
When using Modelsim SE (or PE) or Questasim (tested with QuestaSim 10.5c)
  Go to the folder ../simulation/mentor
  Run ‘Sim.do’ do compile and simulate everything (when there are no libraries yet)
  Run ‘Resim.do’ when libraries already exist to re-compile only the design files and simulate the testbench
The simulation files can be found in the ‘simulation/mentor’ directory
After lane alignement has been achieved the testbench will also insert 2 errors (each resulting in 4 biterrors) which are reported by the testbench.

## Slide 48: Deliverables
Quartus 18.1.1 archive (B263) which contains the demo design files, the software source files, ttk_helper_s10tx.tcl scripts and the testbench files.
The testbenches can be found after restoring the archive: <restored_project>/simulation
The software source files can be found after restoring the archive in the <restored_project>/software/app and <restored_project>/software/bsp folders/
The software executables.
SOF File.
ttk_helper_s10tx.tcl file in the /scripts folder
This document.

## Slide 49: Status & Revision
V18.1.1: February 12th 2019
  Initial release
  Succesfully tested with 5 meter DAC cable at default rate of 53.125 Gbps as well as with overclocked speed of 57.8 Gbps.
  Note that once you move from external loopback back from serial loopback, you will get a very large number of corrected errors. This is known behaviour and will be fixed in a future software update.

## Slide 50: Feedback and/or Questions?
Peter Schepers (peter.schepers@intel.com )
+32 495 57 32 22