## Slide 1: Stratix10 TX Soft PRBS + Dynamic reconfiguration Demo Design V18.1.0 for the Stratix10 TX SI Board 2 Lanes @ up to 57.8 Gbps (PAM4/NRZ) routed to the SMA connectors
Peter Schepers
Technology Specialist FAE High Speed Interfaces
February 27th, 2019

## Slide 2: Introduction & Motivation
This design illustrates how to use the Dynamic reconfiguration capabilities of the E-tile transceiver
Encoding can be dynamically changed from NRZ to PAM4 (separate for Tx and Rx)
Datarate can be dynamically changed (separate for Tx and Rx).
Default configuration is a Native PHY configured in high datarate PAM4 with 2 physical lanes at 56 Gbps.
SoftPRBS data generators and checkers are being used to test the traffic. Generators and checkers operate on 128 bit datapath.

## Slide 3: ‘Soft PRBS/Dynamic Reconfig Demo Design
Goals :
  Demonstrate the dynamic reconfiguration flexibility on Stratix10 TX using Native PHY
    Use Stratix10 TX Signal Integrity board as platform for demonstration.
      Uses Native PHY with 2 physical lanes connected to SMA_A and SMA_B
      This design is ideally suited to measure eye diagrams with a scope (realtime or sampling scope). For sampling scope one of the lanes needs to be configured in NRZ “clock” mode to act as sampling clock.
    Default Line rate in this demo is 57.8 Gbps per lane and PAM4 but using dynamic reconfiguration it can be reconfigured to NRZ or another rate dynamically and on Tx and Rx separately. So Tx can run PAM4 while Rx operates in NRZ mode e.g.
    User data width is 128-bits per lane. On the receive side a deskew module is used to properly deskew the data from the AIB (this is mandatory).
    The user data is generated based on the 451.625Mhz clock (default) generated by the Native PHY (line rate divided by 128).

## Slide 4: Goals (continued)
Goals :
  To create the 2x 128 bit user data 128-bit soft PRBS generators and 128-bit PRBS checkers are being used.
  PRBS Patterns that can be configured are PRBS-13, PRBS-23 and PRBS-31. A clock pattern “0F0F….” can also be generated (useful for providing clock to sampling scope).
  Uses Reconfiguration Management Interfaces for the E-tile transceiver.
  Through ADME Transceiver Toolkit support is automatically available.
  Use Nios II processor as controller/monitor.
  Reports errorcount and calculates BER based on the received data.
  Includes Testbench

## Slide 6: E-Tile Native PHY (TX PMA/RX PMA)

## Slide 7: E-Tile Native PHY (Core Interface)

## Slide 8: E-Tile Native PHY (PMA Interface)

## Slide 9: E-Tile Native PHY (Reset/Dynamic Reconfiguration)

## Slide 10: Link Register Set
  The design is using a custom .qsys component that can be parameterized. The component is called “Channel Register Set” (using channel_reg_set_hw.tcl) and is available in the default group section of the Qsys library.
  This component can be parameterized to the number of PHY’s or instances you want to instantiate in your design and makes the generation of the Qsys system much more streamlined.
  As in this design 1 phy’s is being used, the number of register set has been set to 1 in this design.
  For every register set that you use in your design it will generate a number of registers (to control/readout the measured clocks)
  For the AVMM interface to the Native PHY another custom component : “reconfig_mgmt” (reconfig_mgmt_hw.tcl) is being used in this design.

## Slide 11: Timing Closure
The design is fully constraint and has no timing violations.
Compiled for 1ST280EY2F55E2VGS1

## Slide 12: ADME Interface
In addition to the AVMM interfaces the ADME interface (Altera Debug Master Endpoint) is also enabled by default in the Ethernet HIP
Access to the ADME interface can be done through System Console totally in parallel while the Nios controller is also being used.
The ADME interface can be used for advanced debugging and reporting (see further) .
One advantage of having the ADME interface is that it allows to run directly the Transceiver Toolkit (see further).

## Slide 13: Nios II Control & Monitoring
The Nios II controller is used to control and monitor the design using the Nios II terminal.
  Display status signals (for each “Phy”)
    Freq_Locked
    Pll_locked
    PrbsLocked
    Datarate measured based on measured clock frequency (each tx_clkout and rx_clkout is being individually measured).
  Control Serial Loopback on all lanes.
  Dynamically change NRZ to PAM4 on a per channel and per direction basis (so can be different on Tx and Rx in the same transceiver)
  Dynamically change datarate on transmitter on a per channel basis (based on multiplier of the referenceclock)
  Dynamically change datarate on receiver on a per channel basis (based on multiplier of the referenceclock)
  Generate single biterrors in the generated data
  Displays the number of biterrors and the BER.
Access is through Nios SDK shell (see further)

## Slide 14: Nios 2 Output in Nios II SDK Shell (start screen at default speed of 57.8 Gpbs)

## Slide 15: Status With SMA cables connected in “cross”
Connection SMA_A Tx to SMA_B Rx and SMA_B Tx to SMA_A RX results are shown on the right side (using PAM4 at 57.8 Gbps)

## Slide 16: Status With SMA cables connected in “cross”
Connection SMA_A Tx to SMA_B Rx and SMA_B Tx to SMA_A RX results are shown on the right side (using PAM4 at 53.125 Gbps)
Errorfree!

## Slide 17: Reconfigure Tx(0) and Rx(1) to NRZ

## Slide 18: Divide datarate NRZ Tx(0) and Rx(1) by 2

## Slide 19: Available commands

## Slide 20: Board setup (1/2)
Connect SMA’s cables to equipment or between SMA_A and/or SMA_B.
Connect USB Cable to CN1 in order to use onboard USB-Blaster II.
Power on the board
Program the clocks using the Clock control GUI (see screenshot on next page, clocks highlighted in yellow
Download ‘Devkit_Demo.sof’ to the 1ST280EY2F55E2VGS1 device using QII 18.1.2 programmer

## Slide 21: Board setup (2/2)

## Slide 22: Running the software (Option 1)
The programming file already contains the program running on the Nios. To connect to the design do the following
Open a command prompt and run “nios2-terminal -c 1”
(if not already in the $path variable the nios2-terminal.exe can be found in the Quartus installation e.g. C:\quartus_18_1\quartus\bin64)

## Slide 23: Running the software (Option 2)
This is when you want to run a newer version of software (i.e. more recent to the version contained in the .sof file)
Do the following :
  Start a Nios II command Shell (can be found in the Quartus installation (e.g. C:\quartus_18_1\nios2eds) and go to the directory where the .elf file and run.bsh file is located.
  Type In The Following Command : “./run1.bsh” This will set the JtagSpeed to 16M and download the Nios II code to the FPGA and open up the terminal.

## Slide 24: Rebuilding the software (optional)
In order to rebuild the software do the following (using QII 18.1.2 B277 or later):
Start a Nios II 18.1 Command Shell and go to the ../software/app/Stratix10GX_xCh directory (which is part of the archive) and type: ./create-this-app .This will compile the system libraries (in the bsp folder), compile the software code (main.c and a number of other .c files in this case) and produce a Nios II executable.
If you make any changes to the software you need to rebuild by typing “make” in the Nios II 18.1 shell (after having created the software a first time)

## Slide 25: Use of ADME (Optional)
To access the ADME, open the System Console.
Please download or start first the Nios design as otherwise access to system console might be compromised.
From here you have access to all AVMM registers from the transceivers.

## Slide 26: Ttk_helper_s10tx.tcl Script
In the folder “scripts” one can find a useful ttk_helper_s10tx.tcl file that has a library of procedures similar to the ones used in software, ranging in complexity from reading a register to performing adaptation on all channels at the same time.
Most of the procedure require to identify the “phy” on which the action to perform. To identify the “phy” one can just use a unique string that identifies the native phy as it exists in the RTL code.
When sourcing the ttk_helper_s10tx.tcl script you will get the identification automatically and the slave address helps identifying the PHY in the TTK.
Below is the list of E-tile PHY's claimed
Use etile_phy_<i> as phy identifier in the functions
Phy : "etile_phy_22" ---> Hierarchy Path: inst2|xcvr_txrx_inst|xcvr_native_s10_etile_0|alt_xcvr_native_optional_rcfg_logic Slave: 0x800000

## Slide 27: Ttk_helper_s10tx Script (continued)
So to identify PHY1 one can simply use etile_phy_22 e.g. to address that specific phy.
The list on the following slides shows the available procedures and provides examples how to use them.

## Slide 28: ttk_helper_s10tx.tcl Script (Generic functions)
rmw_all {offset mask newval verbose}
example useage rmw_all 0x160 0x0E 0x03 1
rmw_channel {phy channel offset mask newval verbose}
example useage rmw_channel transceiver_block:0 0 3 0x40000 0x0F 0x03 1
rd_channel {phy channel offset verbose}
to read and printout use e.g. rd_channel etile_phy_36 3 0x40000 1
when only reading without printing use e.g. set d [rd_channel etile_phy_36 3 0x40000 0]
rd_all {offset}
example useage rd_all 0x40011
raw_dump_channel {phy ch start_addr stop_addr}
example useage raw_dump_channel etile_phy_36 0 0x000 0x300
compare_xcvr_channels {phy ch1 ch2 start_addr stop_addr}
example useage compare_xcvr_channels etile_phy_36 0 1 0x0 0xF

## Slide 29: Ttk_helper_s10tx Script (E-Tile specific part 1)
rcfg_etile {phy channel interrupt_code interrupt_data verbose}
example useage reading vod : set readback_vod [rcfg_etile etile_phy_36 0 0x15 0x4100 1]
example useage writing vod setting 3 : set readback_vod [rcfg_etile etile_phy_36 0 0x15 0x4003 0]
start_check_prbs_etile {phy channel pattern verbose}
example to start prbs31 on channel 1 of etile_phy_37 : start_check_prbs_etile etile_phy_37 1 31 1
set_serial_loopback_etile {phy channel serial_loop verbose}
example to set serial loopback on channel 4 of etile_phy_36 : set_serial_loopback_etile etile_phy_36 4 1 1
set_mode_etile {phy channel line_encoding tx_clk_divider rx_clk_divider gray_encoding encoding_1_1plusd verbose}
example to set PAM4 on channel 4 of etile_phy_36 with gray_encoding : set_mode_etile etile_phy_36 4 PAM4 0x64 0x64 1 0 1

## Slide 30: Ttk_helper_s10tx Script (E-Tile specific part 2)
iadp_channel {phy channel verbose}
example to run iadp on channel 1 of etile_phy_36 iadp_channel etile_phy_36 1 1
iadp_phy {phy verbose}
example to run iadp at once on all channels of etile_phy_36 : iadp_phy etile_phy_36 1
set_serial_loopback_phy_etile {phy serial_loop verbose}
example to turn serial loopback ON for all channels of etile_phy_36 : set_serial_loopback_phy_etile etile_phy_36 1 1
precal {phy prbspattern line_encoding tx_clk_divider rx_clk_divider gray_encoding encoding_1_1plusd verbose}
example to run precal with prbs31 with pam4 on on all channels of etile_phy_37 : precal etile_phy_37 31 PAM4 0x64 0x64 1 0 1
precal_simple {phy prbspattern exit_mode verbose}
example to run precal with prbs31 on all channels of etile_phy_37 and turn off prbs31 after calibration : precal_simple etile_phy_37 31 OFF 1
get_firmware {phy}
example to get firmware version : get_firmware etile_phy_36

## Slide 31: Using Transceiver Toolkit (Optional)
To start the Transceiver Toolkit simply start it from the Tools Menu in Quartus (with the project loaded). Using 18.1 or later.
This will automatically detect the design and start up the Transceiver Toolkit which allows you to run further tests in optimizing the PMA settings, do autosweeps etc.
Note that when the TTK is launched a short burst of errors is introduced on the transceivers (this is a known issue pending investigation)
Make sure to stop all traffic running in TTK and close the TTK before going back to the Nios terminal to continue with the design.

## Slide 32: Signaltap II Debug Example
The design contains a number of signaltap instances
Signaltap II acquisition can be done simultaneously with Nios II control.

## Slide 33: TestBench
First use : Open a Nios II 18.1 Shell and go to the simulation directory. In the shell provide the following command “./create_simscript.bsh”. This will create the necessary simulation scripts to match your own environment.
When using Modelsim SE (or PE) or Questasim (tested with QuestaSim 10.5c)
  Go to the folder ../simulation/mentor
  Run ‘Sim.do’ do compile and simulate everything (when there are no libraries yet)
  Run ‘Resim.do’ when libraries already exist to re-compile only the design files and simulate the testbench
The simulation files can be found in the ‘simulation/mentor’ directory
After lane alignement has been achieved the testbench will also insert 2 errors (each resulting in 4 biterrors) which are reported by the testbench.

## Slide 34: Deliverables
Quartus 18.1.2 archive (B277) which contains the demo design files, the software source files, ttk_helper_s10tx.tcl scripts and the testbench files.
The testbenches can be found after restoring the archive: <restored_project>/simulation
The software source files can be found after restoring the archive in the <restored_project>/software/app and <restored_project>/software/bsp folders/
The software executables.
SOF File.
ttk_helper_s10tx.tcl file in the /scripts folder
This document.

## Slide 35: Status & Revision
V18.1.2: February 27th 2019
  Documented release
  Upgraded to 18.1.2
  Succesfully tested with “cross-configuration” of SMA-Loopbacks and using dynamic reconfiguration of encoding (NRZ or PAM4) and datarate.

## Slide 36: Feedback and/or Questions?
Peter Schepers (peter.schepers@intel.com )
+32 495 57 32 22