## Slide 1: Stratix10 TX ‘Superlite II V4’ Demo Design V18.1 for the Stratix10 TX SI Board 8 Lanes @ 28.3 Gbps routed to the QSFP-DD modules
Peter Schepers
Technology Specialist FAE High Speed Interfaces
November 5th , 2018

## Slide 2: Introduction & Motivation
This design illustrates how to use the Superlite II V4 concept on Stratix10 TX using the E-Tile
The V4 version of Superlite II is based on the V2+V3 version. The V2 version uses a valid signal in combination with the transmit data and there is also a ready signal provided which can potentially halt the transmit traffic for a short interval (based on filling level of Transmit FIFO). This interface is equivalent to the Avalon Streaming Interface.
The V3 version adds additional functionality :
  Link information is exchanged between the local and remote side and results in a LinkUp when both local and remote side are aligned.
  XOFF is used in order to allow for backpressure or Flow Control: ask remote side to stop sending traffic (when local side e.g. is not capable of receiving the data).
  Because of the exchanges between local and remote side the protocol is now a fully bidirectional protocol (V1 and V2 versions could be used fully unidirectional)
  The V4 version is the E-tile version where everything is clocked with a single clock.
  This specific version is using 2 instances of the Superlite II V4 demo, each with 4 lanes running at 28.3 Gbps and each connected to the lower lanes of the 1x2 QSFP-DD module. Using DAC or Fiber Optic connection a full system test can be done between the 2 modules, illustrating link-up, reset behaviour etc.

## Slide 3: How to use Superlite II V4 in Packet mode ?
  By nature the Superlite II V4 is using streaming data (Avalon streaming based) so not framed or packetized . One could however support also a framed mode (or packet mode) by using one of the lanes to transport the packet related information (SOP, EOP, etc) . This does require an additional lane to provide the packet overhead information. This concept has been succesfully implemented on Stratix V GX (with 11 lanes) and can easily be repeated on Stratix10 (with higher rates and including KR-FEC).

## Slide 4: ‘Superlite II V4’ Concept

## Slide 5: ‘SuperLite II V4’ Concept
Transport data from point A to point B as simple as possible multiple bidirectional serial links. Note that the number of lanes in each direction do not have to be equal.
V3 version of the protocol exchanges information between local and return side (handshaking) as well as XON/XOFF control (backpressure)
On the transmit side data will only be written in the FIFO when the valid signal is asserted, the fifo also can issue a backpressure signal (indicated by the ‘ready’ signal to indicate if data can be transmitted. This is equivalent to the Avalon Streaming interface.
When XOFF is received from the remote side, all traffic will be halted on the local side (link remains up though).
All the logic is clocked on one single clock (i.e. both transmit and receive core logic), this clock is the clock derived from the transmit PLL and is basically the line rate/64.
This implies that the combination of data valid with the locally generated clock from the local transmit PLL is frequency locked to the clock used at the transmit side (which will typically vary in ppm).
Uses 64/66 Encoding in combination with scrambling.
Multiple lanes are bonded, there is no real limit on the number of lanes that can be used, apart from potential limitations to compile very large number of lanes. Typically 4 or 10 lanes will be used. Also a single lane is possible.

## Slide 6: ‘Superlite II V4’ Concept (continued)
For word alignment and lane alignment idle characters and alignment characters will be sent at regular intervals based on the filling level of the Fifo at the transmit side.
The Superlite II V4 TX module will automatically pause Tx user data if needed to insert idle and alignment characters and will also pause Tx user data based on the “ready” received from the Native PHY (as it is working in overspeed). So the userdata needs to be able to immediately stop sending traffic. If this is not possible one can add an additional FIFO with a slower running write clock.
User data is always 64 bit per lane because of the 64b66b encoding.

## Slide 7: ‘SuperLite II V4 2x4 lanes Demo Design
Goals :
  Demonstrate the Superlite II V4 concept on Stratix10 TX
    Use Stratix10 TX Signal Integrity board as platform for demonstration.
      Uses 2 Superlite II V4 demo instances (each with their own packet generator and checker). Each instance (or “phy”) is connected to the QSFP-DD module
      Full system validation can be done using either a DAC cable (various length) or Fiber Optic connection using the 2 QSFP28 modules.
    Line rate in this demo is 28.3 Gbps per lane by default but it could run slower if required.
    4 lanes will be used for each phy, therefore aggregate line rate is 113.2 Gbps per phy
    User data width is 256-bits (64 bits per lane) per phy
    Actual throughput depends on the configured “read time” and “idle time” parameters. In the demo the “read time” is 1056 clock cycles and “idle time” is 7 clock cycles but these can be easily changed. The “read time” needs to be an integer multiple of 33.
    Actual throughput is measured in the design by measuring the data_valid received in combination with the clock.

## Slide 8: Goals (continued)
Goals :
    The user data is generated based on the line_rate/64 Mhz clock generated by the Native PHY . As it receives backpressures from the Superlite IV Tx module the data will be halted at specific times.
    To create the 256 bit user data in each phy a combination of different counterpatterns and prbspatterns are used across the 4 lanes of each phy
  Through ADME Transceiver Toolkit support is automatically available.
  Use Nios II processor as controller/monitor.
  The RAM in the QSYS is programmed with the latest software, so one can directly connect to the system using JTAG and run the software.
  Reports errorcount and calculates BER based on the received data.
  Includes Testbench

## Slide 9: ‘Superlite II V4’ Resources (one phy)
Superlite II V4 Etile TxRx Module Resources 4 lanes at 28.3 Gbps.
  ~ 2800 ALUT’s
  ~ 2100 ALM’s
  ~ 4800 Dedicated logic registers
  15 M20K (for the receive and transmit buffers)

## Slide 11: ‘txrx_pcs_64b66b_Etile’ Detailed blockdiagram

## Slide 12: Tx Path
A datastream is generated at a clock of 442.1875 Mhz @ 256 bits when DataIn_ready is high. The datapattern is a combination of 4 60-bit Prbs-23 (each with their own starting value) and one 16-bit counterpattern.
  The 16-bit counterpattern is spread across the 16 lanes, 4 bits per lane. This is to make sure any deskew on the lanes would be immediately spotted.
Since idle +alignment characters have to be inserted at regular intervals and because of the overclocking the pcs is generating periodic tx_pcs_ready pulses the data stream will be halted at regular intervals. This is indicated by the Superlite IV TX module by the DataIn_ready signal.
Single biterrors can be inserted using inserterror input. As there is one PRBSGenerator per virtual lane, the biterror insert will produce 4 bit-errors at a time.
This data is presented to the Superlite II Tx Module
The data is written into the TxFifo (single clocked fifo) using the 442.1875 Mhz as clock and using the DataIn_Valid as write-enable.
The read_enable is pulsed at the same pace as the write-enable.
If no valid data is present idle characters will be sent.

## Slide 13: Tx Path (continued)
The 64b66 encoding is very straightforward : bits 65..64 are set to “10” for control data and “01” for data (so neutral disparity)
In terms of idle character a value of “1C1C….1CBC” is being used. The alignment character is sent as the last control character. The lower 16 bits of this control word (at the alignment position) encodes the status of the link in addition to the alignment indication.
If no local alignment has been found : the last control word sent is “..7C7C”
If local wordalignment has been found : the last control word sent is “..FD7C”
If XOFF is being sent to the remote side : the last control word sent is “..5C7C”
If local side is not transmitting : the last control word sent is “..3C7C”
If local side is not transmitting and XOFF is being sent to the remote side : last control word sent is “…9C7C”.

## Slide 14: Tx Path (continued)
In order to make sure there is DC balance and enough transitions present on the serial links a selfsynchronizing scrambler is used (the same as being used in 10GbE). The scrambler will scramble only the 64 databits (the framing bits on bits [65..64] are not scrambled since they are required for the framing. The polynomial used for the scrambler is 1 + x^39 + x^58 according to the IEEE.
The resulting 66-bit is sent to the Native PHY where the gearbox converts it from 66-bit to 64-bits PMA
Finally the data is serialized (using 64-bit serializer) and sent out as serial datastreams (28.3 Gbps per lane).

## Slide 15: Rx Path
After deserialization the data and passing to the gearbox the 66 bits data per lane is presented to the 64b66b decoder module which will periodically assign bitslips until correct frame alignment has been achieved.
This is all happening on all lanes at the same time and everything is clocked based on the recovered clock of channel 0. The FIFOs inside the Native PHY will be used to make sure lanes 1 to 4 have the right phaserelationship. Note that the recovered clock on lanes 1 to 4 are the same frequency as lane 0 but have a different phase relationship.

## Slide 16: Rx Path (continued)
Based on the position of the alignment word, the delay for each lane is measured, the statemachine inside the Rx_path_deskew module will use the information of that measured delay to control a special Rx FIFO signal “rx_fifo_rd_en” on all RxFIFO’s instantiated externally to deskew all the lanes.
Once lane alignment is achieved the 256-bit combined data in addition with a data valid signal will be sent to the data verifier.
Here PRBS and counterverification will take place and single biterrors will be counted.
Prbslocked is asserted when 128 consecutive valid Prbs-23 60-bit words have been received on each of the lanes and de-asserted when 128 consecutive non-valid Prbs-23 60-bit words have been received.
Countlocked is asserted when 128 consecutive valid 16-bit counter words have been received on the parts of the lanes they were received.
There are 4 60 bit PRBS Verifiers (one for every lane) and 1 16-bit CountVerifiers to validate the 256 bit data.

## Slide 17: Rx Path (continued)
The V3 version adds an additional Rx State machine to the logic to determine the local Rx state and it depends on the incoming “alignment” control word
If last control word received is “…FD7C” it means the remote side has reached Wordalignment, if local side also has reached wordalignment this results in Linkup to be asserted, indicating that both sides are up and running. This can be used as the trigger to sent data across e.g.
If last control word received is “…5C7C” it means an XOFF has been received from the remote side, this will be forwarded to the local transmitter to stop generating traffic on the local side.
If last control word received is “…3C7C” it means the remote side has stopped sending traffic (as a response to a local XOFF)
If last control word received is “…9C7C” it means the remote side has stopped sending traffic but at the same time also requesting XOFF. At this point of time both local and remote side are not generating any traffic (Link is still up).

## Slide 18: Native PHY (TX,RX PMA settings)

## Slide 19: Native PHY (Core Interface)

## Slide 20: Native PHY (PMA Interface)

## Slide 21: Native PHY (Reset)

## Slide 22: Native PHY (Dynamic Reconfiguration)

## Slide 23: Link Register Set
  The design is using a custom .qsys component that can be parameterized. The component is called “Link Register Set” (using link_reg_set_hw.tcl) and is available in the default group section of the Qsys library.
  This component can be parameterized to the number of PHY’s you want to instantiate in your design and makes the generation of the Qsys system much more streamlined.
  As in this design 2 phy’s are being used, the number of link register sets has been set to 2 in this design.
  For every Link that you use in your design it will generate a number of registers (to control/readout the measured clocks) as well as the AVMM reconfiguration interface to the Native PHY.
  For that the Link Register set is calling another custom component : “reconfig_mgmt” (reconfig_mgmt_hw.tcl) which provides those AVMM interfaces to the Native PHY

## Slide 24: ADME Interface
In addition to the AVMM interface the Native PHY also enables the ADME interface (Altera Debug Master Endpoint) which can also be accessed through the Qsys system due to the addition of the jtag_debug_module.
Access to the ADME interface can be done through System Console totally in parallel while the Nios controller is also being used.
The ADME interface can be used for advanced debugging and reporting (see further) .
The major advantage of having the ADME interface is that it allows to run directly the Transceiver Toolkit (see further).

## Slide 25: Timing Closure
The design is fully constraint and has a minor setup time violation of 23 ps which has no impact on functionality. If compilation is done without .stp file, timing is fully met. Compiled for 1ST280EY2F55E2VGS1

## Slide 26: Nios II Control & Monitoring
The Nios II controller is used to control and monitor the design using the Nios II terminal.
  Display status signals
    Freq_Locked
    Pll_locked
    Link Up
    DataLocked (combination of the 4 PrbsLocked and Countlocked)
    WordAligned, LaneAligned
    Effective Datarate
    Efficiency
    Latency (only when looped back on it’s own)
  Control Serial Loopback on all lanes.
  Generate single biterrors in the generated data (note that inserting an error will result in 4 errors being seen : one per lane.
  Displays the number of biterrors and the BER.

## Slide 27: Nios II Control & Monitoring
  Allows to start a continuous BER measurement with a controllable interval (default time interval is 2 seconds).
  Displays the time the test has been running.
  Allows to find the optimum PMA settings (AC gain, EQ Gain, VGA gain, VOD, Pre-emphasis, CTLE Offset coefficients) using PMA sweep function. (Option ‘U’)
  Displays the measured reference clock frequency (Measured with 100 Mhz reference clock during 1 second).
  Measures the minimum and maximum latency (only when looped back to itself)
Access is through Nios SDK shell (see further)

## Slide 28: Nios 2 Output in Nios II SDK Shell (5 meter DAC)

## Slide 29: Status and PMA settings PHY 0 (5 meter DAC)
0 Biterrors have been observed during the 11 minutes run time

## Slide 30: Status and PMA settings PHY 1 (5 meter DAC)
PHY 1 is also completely errorfree during the 11 minutes of operation.

## Slide 31: Sweep PMA settings
Screenshot below shows option (‘u’) that allows to sweep the transmit PMA settings and perform BER measurement for every step. At the end of the sweep you will get a suggestion on which setting is the best based on BER and BER window. It is up to the user to manually enter which setting to use (can be any setting).
Since the setup requires by default a connection between the 1x2 QSFP-DD modules, when a sweep is done the Tx channel is automatically taken from the corresponding phy.
Following PMA parameters can be swept.

## Slide 32: Sweep PMA settings Example
Sweeping Vod

## Slide 33: Losses associated with 5 Meter DAC cable
Cable used : 5m (16.4') 100GbE QSFP28 Cable - Amphenol 100-Gigabit Ethernet Passive Copper QSFP Cable (SFF-8665 802.3bj) - QSFP28 to QSFP28 (26 AWG)
https://www.cablesondemand.com/category/QSFP%20100G/product/SF-NDAAFJ100G-005M/URvars/Items/Library/InfoManage/.htm
See following slides for measured Insertion loss for both the board and the cable.
Cable insertion loss is ~ 22 dB at 14.2 Ghz.
Board insertion loss (TX+RX) is estimated to be at ~ 8.5 dB at 14.2 Ghz.
Connector insertion loss (estimate : 0.5 dB)
So total insertion loss at 14.2 Ghz (28.3 Gbps) ~ 31 dB.

## Slide 34: Cable Insertion Loss 5 meter DAC Cable

## Slide 35: Available commands

## Slide 36: Measuring Latency
Option ‘M’ is measuring the maximum latency across 1000 resets and provides a histogram of this maximum latency being measured. (this can only be measured when qsfp_to_qsfp is set to 0 in the main.c and an external loopback is used or when all lanes are in serial loopback (this is automatically checked)).
As can be seen latency is on average 70 parallel clock cycles which is 158 ns at 28.3 Gbps.

## Slide 37: Board setup (1/2)
Connect DAC cable (or optical connection) between the 1x2 QSFP-DD Module (U32) and (U75).
Connect USB Cable to CN1 in order to use onboard USB-Blaster II.
Power on the board
Program the clocks using the Clock control GUI (see screenshot on next page, clocks highlighted in yellow), datarate is referenceclock frequency x 100. So 283 Mhz gives you 28.3 Gbps.
Download ‘Devkit_Demo.sof’ to the 1ST280EY2F55E2VGS1 device using QII 18.1 (B222) programmer (use 16 Mhz programming clock frequency in the programmer)

## Slide 38: Board setup (2/2)

## Slide 39: Running the software (Option 1)
The programming file already contains the program running on the Nios. To connect to the design do the following
Open a command prompt and run “nios2-terminal -c 1”
(if not already in the $path variable the nios2-terminal.exe can be found in the Quartus installation e.g. C:\quartus_18_1\quartus\bin64)

## Slide 40: Running the software (Option 2)
This is when you want to run a newer version of software (i.e. more recent to the version contained in the .sof file)
Do the following :
  Start a Nios II command Shell (can be found in the Quartus installation (e.g. C:\quartus_18_1\nios2eds) and go to the directory where the .elf file and run.bsh file is located.
  Type In The Following Command : “./run1.bsh” This will set the JtagSpeed to 16M and download the Nios II code to the FPGA and open up the terminal.

## Slide 41: Rebuilding the software (optional)
In order to rebuild the software do the following (using QII 18.1 B222 or later):
Start a Nios II 18.1 SDK Shell and go to the ../software/app/Stratix10GX_xCh directory (which is part of the archive) and type: ./create-this-app .This will compile the system libraries (in the bsp folder), compile the software code (main.c and a number of other .c files in this case) and produce a Nios II executable.
If you make any changes to the software you need to rebuild by typing “make” in the Nios II 18.1 shell (after having created the software a first time)

## Slide 42: Use of ADME (Optional)
To access the ADME, open the System Console.
Please download or start first the Nios design as otherwise access to system console might be compromised.
From here you have access to all AVMM registers from the transceivers.

## Slide 43: Ttk_helper_s10tx.tcl Script
In the folder “scripts” one can find a useful ttk_helper_s10tx.tcl file that has a library of procedures similar to the ones used in software, ranging in complexity from reading a register to performing adaptation on all channels at the same time.
Most of the procedure require to identify the “phy” on which the action to perform. To identify the “phy” one can just use a unique string that identifies the native phy as it exists in the RTL code.
When sourcing the ttk_helper_s10tx.tcl script you will get the identification automatically and the slave address helps identifying the PHY in the TTK.
Below is the list of E-tile PHY's claimed
Use etile_phy_<i> as phy identifier in the functions
Phy : "etile_phy_17" ---> Hierarchy Path: {\Generate_Superlite_II_Instances:0:instx|superliteii_txrx_module_inst|txrx_pcs_64b66b_inst|xcvr_txrx_inst|xcvr_native_s10_etile_0|alt_xcvr_native_optional_rcfg_logic} Slave: 0x800000
Phy : "etile_phy_18" ---> Hierarchy Path: {\Generate_Superlite_II_Instances:1:instx|superliteii_txrx_module_inst|txrx_pcs_64b66b_inst|xcvr_txrx_inst|xcvr_native_s10_etile_0|alt_xcvr_native_optional_rcfg_logic} Slave: 0x1000000

## Slide 44: Ttk_helper_s10tx Script (continued)
So to identify PHY1 one can simply use etile_phy_18 e.g. to address that specific phy.
The list on the following slides shows the available procedures and provides examples how to use them.

## Slide 45: Ttk_helper_s10tx Script (Generic functions)
rmw_all {offset mask newval verbose}
example useage rmw_all 0x160 0x0E 0x03 1
rmw_channel {phy channel offset mask newval verbose}
example useage rmw_channel transceiver_block:0 0 3 0x40000 0x0F 0x03 1
rd_channel {phy channel offset verbose}
to read and printout use e.g. rd_channel etile_phy_36 3 0x40000 1
when only reading without printing use e.g. set d [rd_channel etile_phy_36 3 0x40000 0]
rd_all {offset}
example useage rd_all 0x40011
raw_dump_channel {phy ch start_addr stop_addr}
example useage raw_dump_channel etile_phy_36 0 0x000 0x300
compare_xcvr_channels {phy ch1 ch2 start_addr stop_addr}
example useage compare_xcvr_channels etile_phy_36 0 1 0x0 0xF

## Slide 46: Ttk_helper_s10tx Script (E-Tile specific part 1)
rcfg_etile {phy channel interrupt_code interrupt_data verbose}
example useage reading vod : set readback_vod [rcfg_etile etile_phy_36 0 0x15 0x4100 1]
example useage writing vod setting 3 : set readback_vod [rcfg_etile etile_phy_36 0 0x15 0x4003 0]
start_check_prbs_etile {phy channel pattern verbose}
example to start prbs31 on channel 1 of etile_phy_37 : start_check_prbs_etile etile_phy_37 1 31 1
set_serial_loopback_etile {phy channel serial_loop verbose}
example to set serial loopback on channel 4 of etile_phy_36 : set_serial_loopback_etile etile_phy_36 4 1 1
set_mode_etile {phy channel line_encoding tx_clk_divider rx_clk_divider gray_encoding encoding_1_1plusd verbose}
example to set PAM4 on channel 4 of etile_phy_36 with gray_encoding : set_mode_etile etile_phy_36 4 PAM4 0x64 0x64 1 0 1

## Slide 47: Ttk_helper_s10tx Script (E-Tile specific part 2)
iadp_channel {phy channel verbose}
example to run iadp on channel 1 of etile_phy_36 iadp_channel etile_phy_36 1 1
iadp_phy {phy verbose}
example to run iadp at once on all channels of etile_phy_36 : iadp_phy etile_phy_36 1
set_serial_loopback_phy_etile {phy serial_loop verbose}
example to turn serial loopback ON for all channels of etile_phy_36 : set_serial_loopback_phy_etile etile_phy_36 1 1
precal {phy prbspattern line_encoding tx_clk_divider rx_clk_divider gray_encoding encoding_1_1plusd verbose}
example to run precal with prbs31 with pam4 on on all channels of etile_phy_37 : precal etile_phy_37 31 PAM4 0x64 0x64 1 0 1
precal_simple {phy prbspattern exit_mode verbose}
example to run precal with prbs31 on all channels of etile_phy_37 and turn off prbs31 after calibration : precal_simple etile_phy_37 31 OFF 1
get_firmware {phy}
example to get firmware version : get_firmware etile_phy_36

## Slide 48: Using Transceiver Toolkit (Optional)
To start the Transceiver Toolkit simply start it from the Tools Menu in Quartus (with the project loaded). Using 18.1 or later.
This will automatically detect the design and start up the Transceiver Toolkit which allows you to run further tests in optimizing the PMA settings, do autosweeps etc.
Make sure to stop all traffic running in TTK before going back to the Nios terminal to continue with the design.

## Slide 49: Demonstration on the board
LED’s
  LED0 : Combined TxPLL_Locked (Transceiver locked to reference clock
  LED1 : Combined Rx_Freqlocked status of selected channel
  LED2 : Combined WordAligned
  LED3 : Combined LaneAligned
  LED4 : Combined Locked (CountLocked and all PRBSLocked signal asserted)
  LED5 : Combined Link OK : Locked + No biterrors
  LED6 : Combined Link Up
  LED7 : Not used

## Slide 50: Signaltap II Debug Example
The design contains a number of signaltap instances, each clocked by it’s own clock.
Signaltap II acquisition can be done simultaneously with Nios II control.

## Slide 51: TestBench
First use : Open a Nios II 18.1 Shell and go to the simulation directory. In the shell provide the following command “./create_simscript.bsh”. This will create the necessary simulation scripts to match your own environment.
When using Modelsim SE (or PE) or Questasim (tested with QuestaSim 10.5c)
  Go to the folder ../simulation/mentor
  Run ‘Sim.do’ do compile and simulate everything (when there are no libraries yet)
  Run ‘Resim.do’ when libraries already exist to re-compile only the design files and simulate the testbench
The simulation files can be found in the ‘simulation/mentor’ directory
After lane alignement has been achieved the testbench will also insert 2 errors (each resulting in 4 biterrors) which are reported by the testbench.
Note that the testbench contains 2 instances of the Ultralite II design to mimic the hardware setup and to validate the system implementation.

## Slide 52: Deliverables
Quartus 18.1 archive (B222) which contains the demo design files, the software source files, ttk_helper_s10.tcl scripts and the testbench files.
The testbenches can be found after restoring the archive: <restored_project>/simulation
The software source files can be found after restoring the archive in the <restored_project>/software/app and <restored_project>/software/bsp folders/
The software executables.
SOF File.
ttk_helper_s10tx.tcl file in the /scripts folder
This document.

## Slide 53: Status & Revision
V18.1: November 5th 2018
  Initial release
  Succesfully tested with 5 meter DAC cable.

## Slide 54: Feedback and/or Questions?
Peter Schepers (peter.schepers@intel.com )
+32 495 57 32 22